## Slide 1: Number System and Conversion
350151- Digital Circuit
Choopan Rattanapoka

## Slide 2: Introduction
Many number systems are in use in digital technology. The most common are :
  Decimal (Base 10)
  Binary (Base 2)
  Octal (Base 8)
  Hexadecimal (Base 16)
The decimal system is the number system that we use everyday

## Slide 3: Number System
Decimal system uses symbols (digits) for the ten values 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
Binary System uses digits for the two values 0, and 1
Octal System uses digits for the eight values 0, 1, 2, 3, 4, 5, 6, 7
Hexadecimal System uses digits for the sixteen values 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
to represent any number, no matter how large or how small.

## Slide 4: Decimal System
The decimal system is composed of 10 numerals or symbols. These 10 symbols are 0,1,2,3,4,5,6,7,8,9; using these symbols as digits of a number, we can express any quantity.
Example : 3501.51
3 | 5 | 0 | 1 | . | 5 | 1
digit
decimal point
Most Significant Digit
Least Significant Digit

## Slide 5: Binary System
The binary system is composed of 2 numerals or symbols 0 and 1; using these symbols as digits of a number, we can express any quantity.
Example : 1101.01
1 | 1 | 0 | 1 | . | 0 | 1
bit
binary point
Most Significant
Bit
Least Significant Bit

## Slide 6: Decimal Number Quantity (positional number)
3 5 0 1 (base-10)
1 X 100 = 1
0 X 101 = 0
5 X 102 = 500
3 X 103 = 3000
3000 + 500 + 0 + 1 = 3501

## Slide 7: Binary-to-Decimal Conversion
1 1 0 1 (base-2)
1 X 20 = 1
0 X 21 = 0
1 X 22 = 4
1 X 23 = 8
8 + 4 + 0 + 1 = 13
11012= 1310

## Slide 8: Octal-to-Decimal Conversion
5 2 1 7 (base-8)
7 X 80 = 7x1 = 7
1 X 81 = 1x8 = 8
2 X 82 = 2x64 = 128
5 X 83 = 5x512 = 2560
2560 + 128 + 8 + 7 = 2703
52178 = 270310

## Slide 9: Hexadecimal-to-Decimal Conversion
1 A C F (base-16) [ A = 10, B = 11, C = 12, D = 13, E = 14, F = 15 ]
15 X 160 =15x1 = 15
12 X 161 =12x16 = 192
10 X 162 =10x256 = 2560
1 X 163 = 5x4096 = 20480
20480 + 2560 +192 + 15 = 23247
1ACF16 = 2324710

## Slide 10: Decimal Number Quantity (fractional number)
. 5 8 1 (base-10)
5 X 10-1 = 5x0.1 = 0.5
8 X 10-2 = 8x0.01 = 0.08
1 X 10-3 = 1x0.001 = 0.001
0.5 + 0.08 + 0.001 = 0.581

## Slide 11: Binary-to-Decimal Conversion
. 1 0 1 (base-2)
1 X 2-1 = 1x0.5 = 0.5
0 X 2-2 = 0x0.25 = 0
1 X 2-3 = 1x0.125 = 0.125
0.5 + 0 + 0.125 = 0.625
0.1012 = 0.62510

## Slide 12: Octal-to-Decimal Conversion
. 2 5 (base-8)
2 X 8-1 = 2x0.125 = 0.25
5 X 8-2 = 5x0.015625 = 0.017825
0.25 + 0.017825 = 0.267825
0.258 = 0.26782510

## Slide 13: Hexadecimal-to-Decimal Conversion
. F 5 (base-16)
15 X16-1 = 15x0.0625 = 0.9375
5 X16-2 = 5x0.00390625 = 0.01953125
0.9375 + 0.01953125 = 0.95703125
0.F516 = 0.9570312510

## Slide 14: Exercise 1
Convert these binary system numbers to decimal system numbers
  100101101
  11100.1001
  111111
  100000.0111

## Slide 15: Decimal-to-Binary Conversion (positional number)
2 5 0
250
2
125
2
Remainder 0
62
2
Remainder 1
31
2
Remainder 0
15
2
Remainder 1
7
2
Remainder 1
3
2
Remainder 1
1
Remainder 1
25010 = 1 1 1 1 1 0 1 02

## Slide 16: Decimal-to-Octal Conversion
2 5 0
250
8
31
8
Remainder 2
3
Remainder 7
25010 = 3728

## Slide 17: Decimal-to-Hexadecimal Conversion
2 5 0
250
16
15
Remainder 10
25010 = 15 1016 ?
= FA16

## Slide 18: Decimal-to-Binary Conversion (fractional number)
0 . 4375
0.4375 x 2 = 0.8750
0.8750 x 2 = 1.75
0.75 x 2 = 1.5
0.5 x 2 = 1.0
0.437510 = 0.01112

## Slide 19: Decimal-to-Octal Conversion
0 . 4375
0.4375 x 8 = 3.5
0.5 x 8 = 4.0
0.437510 = 0.348

## Slide 20: Decimal-to-Hexadecimal Conversion
0 . 4375
0.4375 x 16 = 7.0
0.437510 = 0.716

## Slide 21: Example :Decimal-to-Binary Conversion (Estimation)
0 . 7 8 2
0.782 x 2 = 1.564
0.564 x 2 = 1.128
0.128 x 2 = 0.256
0.256 x 2 = 0.512
0.512 x 2 = 1.024
0.024 x 2 = 0.048
0.048 x 2 = 0.096
0.192 x 2 = 0.384
0.384 x 2 = 0.768
0.768 x 2 = 1.536
110012  2-1 + 2-2 + 2-5
 0.5 + 0.25 +0.03125
 0.78125
11001000012
 2-1 + 2-2 + 2-5 + 2-10
 0.5 + 0.25 +0.03125 +
0.0009765625
 0.7822265625

## Slide 22: Exercise 2
Convert these decimal system numbers to binary system numbers
  127
  38
  22.5
  764.375

## Slide 23: Base X – to – Base Y Conversion
We can convert base x number to base y number by following these steps :
  Convert base x to base 10 (decimal system number)
  Then, convert decimal number to base y

## Slide 24: Example
Convert 372.348 to hexadecimal system number
  Convert 372.348 to decimal system number
    372.348 = (3x82)+(7x81)+(2x80) . (3x8-1) + (4x8-2)
    = 192 + 56 + 2 . 0.375 + 0.0625
    = 250 . 4375
  Convert 250.437510 to hexadecimal system number
    250.437510
250 / 16 = 15 remainder 10
250  FA16
Positional number
0.4375 * 16 = 7.0
0.4375  0.716
Fractional number
372.348 = FA.716

## Slide 25: Exercise 3 (TODO)
Convert these numbers to octal system number
  11100.10012
  1111112
  5A.B16
Convert these numbers to binary system number
  5A.B16
  75.28