## Slide 1: Negative Binary Number
350151 – Digital Circuit 1
Choopan Rattanapoka

## Slide 2: Representing Negative Numbers in Binary
Up to this point, we have not been discussed how to represent negative numbers in binary.
Ex: 510 – 710 = -210 How to represent in binary ?
There are several representation :
  Signed-magnitude representation.
  2’s complement representation (radix complement)
  1’s complement representation (reduced radix complement)

## Slide 3: Signed-Magnitude
It’s the simplest representation for negative binary numbers.
In most computers, in order to represent both positive and negative numbers. The first bit is used as a sign bit.
  0 used for plus.
  1 used for minus.
Thus, for n-bit word, the first bit is the sign bit and n-1 bits represent the magnitude of the number.
1 0 0 0 0 0 0 0
Sign bit Magnitude

## Slide 4: Example
Use signed-magnitude representation to represent these negative decimal numbers (8-bits)
-50
  50  50/2 = 25 remainder 0
  25/2 = 12 remainder 1
  12/2 = 6 remainder 0
  6/2 = 3 remainder 0
  3/2 = 1 remainder 1
  50  1 1 0 0 1 0
   0 1 1 0 0 1 0 ( add 0 to make magnitude 8 bits)
  -50  1 0 1 1 0 0 1 0 (add sign bit [1 for negative])

## Slide 5: Exercise 1
Transform these decimal numbers to signed-magnitude representation.
  4 bits
    -5
    -2
  8 bits
    -100
  16 bits
    -256

## Slide 6: 1’s Complement (1)
The 1’s complement of an N-digits binary integer B:
1’s complement = (2N – 1) – B
Example : Convert -510 to 4-bit 1’s complement
1’s complement = (24 – 1) – 5
= (16 – 1) – 5
= 1010  10102
-510 = 10102

## Slide 7: 1’s Complement (2)
Example : Convert -120 to a 8-bit 1’s complement representation
1’s complement = (28 – 1) – 120
= 256 – 1 – 120
= 13510  1000 01112
Let’s look again to simplify 1’s complement representation.
For 4-bits For 8-bits
  5  0101 120  01111000
  -5  1010 -120  10000111

## Slide 8: Exercise 2
Transform these decimal numbers to 1’s complement representation.
  4 bits
    -5
    -2
  8 bits
    -100
  16 bits
    -256

## Slide 9: 2’s Complement (1)
Generating 2’s complement is more complex than other representations.
However, 2’s complement arithmetic is simpler than other arithmetic.
2’s complement = 2N – B , B ≠ 0
0 , B = 0

## Slide 10: 2’s Complement (2)
Example 1: Convert -510 to 4-bit 2’s complement
2’s complement = 24 – 5
= 16 – 5
= 1110  10112
-510 = 10112
Example 2: Convert -12010 to 8-bit 2’s complement representation
2’s complement = 28 – 120
= 256 – 120
= 136  1000 10002
-12010 = 100010002

## Slide 11: 2’s Complement (3)
Another method to calculate 2’s complement
  Convert number to 1’s complement
  Then, add 1 to that number
Example : Convert -12010 to 8-bit 2’s complement representation
12010 = 01111000
1’s complement  10000111 (invert bits)
2’s complement  10000111 + 1 = 100010002
-12010 = 100010002

## Slide 12: 2’s Complement (4)
Another method to calculate 2’s complement
  Keep same bit from LSB  MSB until found “1”
  Do 1’s complement on the rest bits.
Example : Convert -12010 to 8-bit 2’s complement representation
12010 = 01111000
= 10001000

## Slide 13: Exercise 3
Transform these decimal numbers to 2’s complement representation.
  4 bits
    -5
    -2
  8 bits
    -100
  16 bits
    -256

## Slide 14: Exercise 4
Find the equivalent decimal number of when these negative binary numbers are represented by signed-magnitude, 1’s complement, and 2’s complement (8-bit).
  1000 0011
  1011 1100
  1000 1001
  1100 1100

## Slide 15: 4 bit Microprocessor
+ N | Positive Integers (all systems) | - N | Sign and Magnitude | 2’s Complement N* | 1’s Complement N
+0 | 0000 | -0 | 1000 | ------- | 1111
+1 | 0001 | -1 | 1001 | 1111 | 1110
+2 | 0010 | -2 | 1010 | 1110 | 1101
+3 | 0011 | -3 | 1011 | 1101 | 1100
+4 | 0100 | -4 | 1100 | 1100 | 1011
+5 | 0101 | -5 | 1101 | 1011 | 1010
+6 | 0110 | -6 | 1110 | 1010 | 1001
+7 | 0111 | -7 | 1111 | 1001 | 1000
 |  | -8 | ------- | 1000 | -------

## Slide 16: Recall binary subtraction
1610 - 510
 100002 – 1012
0 1 1 1 2
1 0 0 0 0
- 1 0 1
1 0 1 1
Binary subtraction is not easy to implement in digital circuit.
Thus, we try to implement the binary addition of negative value instead.

## Slide 17: 1’s Complement Subtraction
1610 – 510  1610 + (– 510)
 1 0 0 0 02 + ( 1 1 0 1 02 )
1 0 0 0 0
+ 1 1 0 1 0
1 0 1 0 1 0
+ 1
0 1 0 1 1  1110

## Slide 18: 2’s Complement Subtraction
1610 – 510  1610 + (– 510)
 1 0 0 0 02 + ( 1 1 0 1 12 )
1 0 0 0 0
+ 1 1 0 1 1
1 0 1 0 1 1  1110
Faster and easier than signed-magnitude and 1’s complement subtraction.

## Slide 19: Overflow and Underflow
Overflow occurs when an arithmetic operation yields a result that is greater than the range’s positive limit of 2N-1 – 1
Underflow occurs when an arithmetic operation yields a result that is less than the range’s negative limit of -2N-1

## Slide 20: Example : overflow
510 + 610 (4-bits 2’s complement)
Note that 4 bits can store +7 to -8
5 0101
+ 6 + 0110
1110 1011  -510
11 ≠ -5 OVERFLOW

## Slide 21: Example : underflow
-510 - 710 (4-bits 2’s complement)
Note that 4 bits can store +7 to -8
-5 1011
+ -7 + 1001
-1210 1 0100  410
-12 ≠ 4 UNDERFLOW

## Slide 22: Exercise 5 (TODO)
Transform these decimal number to negative binary signed-magnitude, 1’s complement, 2’s complement representation (8-bits)
  -10, -98, -142, -200, -215
Find the result of these decimal arithmetic in negative binary signed-magnitude, 1’s complement, 2’s complement representation (8-bits)
  -15 + 5
  200 – 50
  215 – 98
  -25 – 9
  -200 – 215