## Slide 1: Binary Code
350151 – Digital Circuit 1
Choopan Rattanapoka

## Slide 2: Binary Code Decimal
Most computer works internally with binary numbers, However, the input-output generally uses decimal number.
Most logic circuits only accept two-valued signal, the decimal number must be coded in terms of binary signals.

## Slide 3: B.C.D. (4-bit code) : 8-4-2-1 (1)
8-4-2-1 Code
  Sometime calls BCD code.
  Each decimal digit is represented by 4-bit binary number
  N = 8b4 + 4b3 + 2b2 + b1
  Ex : 5  8x0 + 4x1 + 2x0 + 1  0101
Example : 5810
Binary equivalent  1110102
8-4-2-1 Code  5 8
0101 1000  01011000

## Slide 4: B.C.D. (4-bit code) : 8-4-2-1 (2)
Convert 8-4-2-1 back to decimal number
Ex : 1001000100000001
1001 0001 0000 0001
9 1 0 1
Answer : 1001000100000001 = 910110

## Slide 5: B.C.D (4-bit code) : Excess-3
Excess-3 or XS3 based on 8-4-2-1 code but add 3 on each decimal digit before convert it to with 8-4-2-1 style
N + 3 = 8b4 + 4b3 + 2b2 + b1
Example : 5810
5 8
Add 3 on each decimal digit  8 11
8-4-2-1 Code  1000 1011
Thus, Excess-3 of 5810 is 10001011

## Slide 6: Exercise 1
Convert these decimal numbers to binary number, 8-4-2-1 binary code, and Excess-3 binary code:
  25
  128
  200
From these binary codes(8-4-2-1 code, and Execess-3), convert them to decimal numbers:
  10001111
  10110010
  100000010101

## Slide 7: Other B.C.D. codes
5-bit code
  2-out-of-5
  51111
  Shift counter
  86421
More than 5-bit code
  Biquinary code
  543210 code
  Ring counter code

## Slide 8: Gray Code
To represent D decimal values, a Gray code of N bits is required.
  where N >= log2 D
Example : To represent 16 values of decimal number we need at least
  N >= log2 16
  N >= 4
Gray code is also called a minimum changed code because only 1 bit changes value between any two consecutive Gray codes.

## Slide 9: Generating Gray Code : 1st method
0
1
Use alternative mirroring of the pattern
1 bit Gray Code
0
1
Alternative Mirror
1
0
00
01
11
10
Fill 0 on the first part and
Fill 1 on the second part
2-bit Gray code

## Slide 10: Generating Gray Code: 1st Method
00
01
11
10
2-bit Gray code
00
01
11
10
10
11
01
00
000
001
011
010
110
111
101
100
3-bit Gray code

## Slide 11: Generating Gray Code: 2nd method
4-bit Binary
b3 b2 b1 b0
4-bit Gray code
g3 g2 g1 g0
  g0 = b0 b1
  g1 = b1 b2
  g2 = b2 b3
  g3 = b3
= Exclusive-OR
0 0 = 0
0 1 = 1
1 0 = 1
1 1 = 0

## Slide 12: Generating Gray Code: 2nd method
Example: Convert a decimal number 6010 to Gray code.
N >= log2 60 approx. N = 6
We need 6-bit Gray code ( g5 g4 g3 g2 g1 g0 )
Binary equivalent of 6010  111100
g0 = b0 b1 = 0 0 = 0
g1 = b1 b2 = 0 1 = 1
g2 = b2 b3 = 1 1 = 0
g3 = b3 b4 = 1 1 = 0
g4 = b4 b5 = 1 1 = 0
g5 = b5 = 1
Ans : Grey code of 6010 is 100010

## Slide 13: Gray Code to Binary
Example : Convert Gray code100010 to Binary number
Gray code 1 0 0 0 1 0
Binary 1 1 1 1 0 0

## Slide 14: Exercise 2
How many minimum bit do we need for Gray code in order to express 128 decimal values ?
Find Gray codes for the following decimal numbers:
  4
  20
  65
  90
  120
Convert these gray codes to binary number
  001
  11100
  10100
  10101

## Slide 15: ASCII
Many applications of computers require the processing of data which contains numbers, letters, and other symbols.
The common alphanumeric code is ASCII code
(American Standard Code for Information Interchange).
ASCII is 7-bit code

## Slide 16: ASCII standard

## Slide 17: ASCII extension (8-bit)

## Slide 18: Example :
What is the ASCII code for “Hi”.
  H  7210  1001000
  i  10510  1101001
Answer : Hi  10010001101001

## Slide 19: Exercise 3 (TODO)
Find binary, 8421BCD, and Excess-3 of the following decimal numbers:
  32, 128, 210
Find decimal numbers of this 8421 BCD:
  01000111, 10010011
Find decimal numbers of this Excess-3:
  10010100, 10100111
Find Gray codes for the following decimal numbers:
  10, 30, 85
Find decimal numbers of this Gray codes:
  0100, 10001, 110010
Find the ASCII code (7-bit) for theses words :
  L33T, OMG!, YaHoo
Find word from this ASCII code :
  1001001 0010100 1001100 1110101 1110110 0010100 1010101