## Slide 1: Error Detection and Correction
350151 – Digital Circuit 1
Choopan Rattanapoka

## Slide 2: Problems and Solution
Some problems may occur when you transmit digital data. (such as noise)
Thus, the solution that can prevent incorrect digital data during the transmission are
  Error Detection
    the ability to detect the presence of errors caused by noise or other impairments during transmission from the transmitter to the receiver
  Error Correction
    the additional ability to reconstruct the original, error-free data.

## Slide 3: Error Detection
There are several schemes exist to achieve error detection, and they are quite simple.
We need to transmit more bits than in the original data.
Example of error detection schemes
  Repetition schemes
  Parity schemes
  Checksum
  Cyclic redundancy checks
  Hamming distance based checks
  Hash function
  Horizontal and vertical redundancy check

## Slide 4: Repetition Schemes
Given a stream of data that is to be sent, the data is broken up into blocks of bits, and in sending, each block is sent some predetermined number of times.
For example, if we want to send "1011", we may repeat this block three times each.
  Suppose we send 1011 1011 1011
  The receiver receives 1010 1011 1011
  As one group is not the same as the other two, we can determine that an error has occurred.
This schemes is not efficient
If receiver receives 1010 1010 1010 then receiver will think that the data is correct !!

## Slide 5: Parity Schemes (1)
There are 2 types of parity error detection:
  Even parity schemes
  Odd parity schemes
The stream of data is broken up into blocks of bits, and the number of 1 bits is counted.
We add an extra bit called parity bit during the transmission

## Slide 6: Parity schemes (2)
Even parity scheme
  The number of bits “1” including parity bit is EVEN.
  Ex 1 : 10010 parity bit  0
  Ex 2 : 11001 parity bit  1
Odd parity scheme
  The number of bits “1” including parity bit is ODD.
  Ex 1 : 10010 parity bit  1
  Ex 2 : 11001 parity bit  0

## Slide 7: Parity schemes (3)
The sender calculates parity bit and then send it with the data.
When, the receiver receives data and parity bit, it calculate if error occurred during the transmission.
Ex 1: Even parity scheme (data error)
Sender Receiver
  100111 110111 (error)
Ex 2: Even parity scheme (parity error)
Sender Receiver
100111 100110 (error)
However, if there are even number of error bit, the parity scheme can not detect them
Sender Receiver
100111 110011 (correct !!!)

## Slide 8: How to apply parity bit
Transmitting digital System
Receiving digital System
Parity-bit
generator
Error detector
Alarm

## Slide 9: Exercise 1
Find the output (P) of 12 input pulses.
0 1 1 1 1 0 0 1 1 1 1 1
1 1 1 1 1 1 0 0 0 0 0 0
0 1 0 1 1 1 0 0 0 1 1 0
1 1 0 0 1 1 0 0 1 1 1 0
0 0 0 0 1 1 0 0 0 0 1 1
l k j i h g f e d c b a
Even –Parity Bit Generator
B
A
C
D
E
P

## Slide 10: Exercise 2
Find error pulses from 12 input pulses.
1 1 0 1 0 1 0 1 0 1 1 1
0 1 0 0 0 0 1 1 1 1 0 1
0 1 0 0 0 0 1 1 1 0 1 1
1 1 0 0 1 0 1 0 1 1 0 0
0 1 0 0 0 1 1 1 1 0 0 1
l k j i h g f e d c b a
ODD –Parity Bit Error Detector
B
A
C
D
P
Error
Parity
bit

## Slide 11: Error Correction
1-bit parity is used to verify the correctness between the data transmission.
However, it can’t identify the error bit’s position
To correct the error, we use the hamming code
  If we want to transmit r bits, we need to add m bits parity.
  (assume: n = r + m )
  Hamming code can correct an error if
    2m ≥ n + 1
  Example : if we want to transmit 4 bits, we need
    2m ≥ (m + 4) + 1
    2m ≥ m + 5
    m ≥ 3
    3-bit parity

## Slide 12: Hamming code (1)
Parity bits will be put in power of 2 positions.
(1, 2, 4, 8, …) [position start from 1]
Rearrange data bits in order and avoid parity bits position.
Example : for 4-bit data(D4, D3, D2, D1), we need at least 3-bit parity (P3, P2, P1).
  Put parity bits in power of 2 position :
  7 6 5 4 3 2 1
  P3 P2 P1
  Rearrange data bit in order
  7 6 5 4 3 2 1
  D4 D3 D2 P3 D1 P2 P1

## Slide 13: Hamming Code (2)
4-bit data are in position of 7, 6, 5, and 3 digit
Convert it to binary
  D4 : 7  111
  D3 : 6  110
  D2 : 5  101
  D1 : 3  011
Parity bit (P1) use for data bit that LSB of its position is 1.
(in this case : D4, D2, and D1)
Parity bit (P2) use for data bit that second bit from LSB of its position is 1. (in this case : D4, D3, and D1)
Parity bit (P3) use for data bit that third bit from LSB of its position is 1. (in this case : D4, D3, and D2)

## Slide 14: Example : Hamming Code (Even Parity Bit)
D4  1 1  D4
D3  0 0  D3
D2  1 1  D2
P3  (D4 D3 D2 )  0 0  P3  0  (D4 D3 D2 )
D1  1 0  D1
P2  (D4 D3 D1 )  0 0  P2  1  (D4 D3 D1 )
P1  (D4 D2 D1 )  1 1  P1  0  (D4 D2 D1 )
There is an error occurred during the transmission !!
P2 and P1 got wrong parity bit so D1 is error !!
transmission
Sender
Receiver

## Slide 15: Hamming Code (3)
Formal error detection :
  Received parity bits XOR Calculated parity bits
The result of XOR operation shows the error position.
From Example :
  P3 P2 P1
  Received : 0 0 1
  Calculated : 0 1 0
  Error digit : 0 1 1  3 (D1)