## Slide 1: Minterm and MAXTERM Expansions
350151 – Digital Circuit 1
Choopan Rattanapoka

## Slide 2: Combinational Logic Design Using a Truth Table
A
B
C
f
A | B | C | f
0 | 0 | 0 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1

## Slide 3: Minterm
Minterm or Sum of Product (SOP)
For output  1
  We do the product (AND) of input (0 = inverse)
For output  0
  We ignore them
Then, we do sum (OR) of all product
A | B | C | f
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A’BC
AB’C’
AB’C
ABC’
ABC
+
A’BC + AB’C’ + AB’C
+ ABC’ + ABC

## Slide 4: Simplification
A’BC + AB’C’ + AB’C + ABC’ + ABC
A’BC + AB’ + AB
A’BC + A
A + BC (X + X’Y = X+Y)

## Slide 5: Maxterm
Maxterm or Product of Sum (POS)
For output  0
  We do the sum (OR) of input (1 = inverse)
For output  1
  We ignore them
Then, we do product (AND) of all sum
A | B | C | f
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A+B+C
A+B+C’
A+B’+C
(A+B+C)(A+B+C’)(A+B’+C)

## Slide 6: Simplification
(A+B+C)(A+B+C’)(A+B’+C)
(A+B)(A+B’+C)
A + B(B’ +C)
A + BC

## Slide 7: Example1
Design a digital circuit from this truth table
Minterm = A’B + AB = B
Maxterm = (A + B)(A’ + B) = B
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
B
F

## Slide 8: Example 2
Design a binary adder that add two 1-bit binary
Minterm of C = AB
Minterm of D = A’B + AB’ = A B
A | B | C(Carry-out) | D(sum)
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 9: Example 2 : Wiring Diagram

## Slide 10: More than 1-bit binary adder
Example : 2-bit binary adder
Input : A2A1 , B2B1
Output : S2S1 , Cout
A2 | A1 | B2 | B1 | S2 | S1 | Cout
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 1
A2
A1
B2
B1
S2
S1
Cout
COMPLICATE !!

## Slide 11: Full Adder (1)
A
B
Cin
Sum
Cout
1-bit at a time
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Minterm of Sum
A’B’Cin + A’BC’in + AB’C’in + ABCin
Minterm of Cout
 A’BCin + AB’Cin + ABC’in + ABCin

## Slide 12: Full Adder (2)
Minterm of Sum
  A’B’Cin + A’BC’in + AB’C’in + ABCin
  A’(B’Cin + BC’in) + A(B’C’in + BCin)
  A’(B Cin) + A(B Cin)’
  A B Cin
Minterm of Cout
  A’BCin + AB’Cin + ABC’in + ABCin
  (A’Bcin + ABCin) + (AB’Cin + ABCin) + (ABC’in + ABCin)
  BCin + ACin + AB

## Slide 13: Full Adder (3)
FA
A
B
Cin
Sum
Cout
  Sum = A B Cin
  Cout = BCin + ACin + AB

## Slide 14: Full Adder Application
2-bit binary adder
2-bit binary adder using full adder
A2
A1
B2
B1
S2
S1
Cout
FA
FA
A1
B1
A2
B2
S2
S1
Cout
Cout
Cin
Cin = 0

## Slide 15: TODO
From the truth table, find the simplified digital circuit from input (A,B,C) to get an output (F) (both boolean expression and wiring diagram)
USE only 1 AND gate and
1 OR gate
Draw a wiring diagram using full adder modules and not gates to perform binary to 2’s complement conversion
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1