## Slide 1: Karnaugh MAP
350151 – Digital Circuit 1
Choopan Rattanapoka

## Slide 2: Introduction to Karnaugh Map
We can simplify boolean expression by using simplification theorem. However, 2 problems arise
  The procedures are difficult to apply in a systematic way
  It is difficult to tell when you have arrived at a minimum solution
Karnaugh map overcome these difficulties by providing systematic methods for simplifying Boolean expression
Generally, Karnaugh map method is faster and easier to apply than other simplification methods.
Karnaugh map is good for simplifying 2-4 inputs

## Slide 3: A 2-Variable Karnaugh map
A = 0, B = 0
A = 1, B = 0
A = 1, B = 1
A = 0, B = 1

## Slide 4: Using Karnaugh map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
1
0
1
0
A’B’
A’B

## Slide 5: Simplifying with Karnaugh map
1
0
1
0
F = A’

## Slide 6: Exercise 1
From this truth table, simplify it by using karnaugh map
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 7: A 3-variable Karnaugh map

## Slide 8: Using Karnaugh Map
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1
0
0
0
0
1
1
1
A’B
BC’
AC’
F = A’B + BC’ + AC’

## Slide 9: Possibility to simplify
A’
B’
B’C’
C’

## Slide 10: Exercise 2
From this truth table, simplify it by using karnaugh map
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 11: A 4-variable Karnaugh Map

## Slide 12: Using Karnaugh Map

## Slide 13: 7-SEGMENT

## Slide 14: TODO
Design a digital circuit that takes 3-bit binary number(B2B1B0) as input and it has 7 output (a,b,c,d,e,f,g) to display decimal number on 7-segment display
  Digital circuit must be SIMPLIFIED by using Karnaugh map
  7-segment can display decimal number from 0 to 7
3-bit Binary to 7-segment encoder
B2
B1
B0
a
b
e
d
c
f
g