## Slide 1: Course Curriculum
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Asst. Prof. Choopan Rattanapoka
Education
  Ph.D in Computer Science (2008)
  Strasbourg University, France.
  Master degree in Computer Science (2004)
  Strasbourg University, France.
  Bachelor degree in Computer Engineering (2000)
  Kasetsart University, Thailand
  Certificate in Technical Education
  (Electrical and Electronics) [PET-6] (1996) KMUTNB, Thailand
Contact
  E-mail: choopanr@kmutnb.ac.th
  Homepage: http://ect.cit.kmutnb.ac.th/~choopan
  Office: 62 - 612

## Slide 3: Asst. Prof. Dr. Suphot Chunwiphat
Education
  Ph.D in Computer Science (2008)
  Institut National Polytechnique de Grenoble, France.
  Master degree in Electrical Engineering (1998)
  King Mongkut’s Institute of Technology Ladkrabang, Thailand.
  Bachelor degree in Telecommunication Engineering (1994)
  King Mongkut’s Institute of Technology Ladkrabang, Thailand.
Contact
  E-mail: spcp@kmutnb.ac.th
  Office: 62 - 607

## Slide 4: Course syllabus
Review the number systems
Introduction to computer architecture & systems
Introduction to the ARM Processor
Assembly Programming Language
C programming Language
System buses : Interfacing Processors and Peripherals (input/output)
Memory Hierarchy

## Slide 5: Grading System
Midterm examination 35%
Final examination 40%
Class attendant 10%
Exercises 15%
  Total score <= 35  F

## Slide 6: Review the number systems
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 7: Objectives
To understand
  Base of number systems: decimal, binary and hexadecimal
  ASCII code
  Unsigned and signed binary systems

## Slide 8: Number System (1)
The decimal system (base 10) is the number system that we use everyday
But in microprocessors or other digital circuits use the binary system (base 2) why ?
For our point of view, binary are too long to write. Thus, we use hexadecimal or hex number (base 16) instead.
Noise Problem

## Slide 9: Decimal System
The decimal system is composed of 10 numerals or symbols. These 10 symbols are 0,1,2,3,4,5,6,7,8,9; using these symbols as digits of a number, we can express any quantity.
Example : 3501.51
3 | 5 | 0 | 1 | . | 5 | 1
digit
decimal point
Most Significant Digit
Least Significant Digit

## Slide 10: Decimal Number Quantity
1 X 100 = 1
0 X 101 = 0
5 X 102 = 500
3 X 103 = 3000
3000 + 500 + 0 + 1 + 0.5 + 0.01 = 3501.51
103 | 102 | 101 | 100 |  | 10-1 | 10-2
3 | 5 | 0 | 1 | . | 5 | 1
5 X 10-1 = 0.5
1 X 10-2 = 0.01

## Slide 11: Binary System
The binary system is composed of 2 numerals or symbols 0 and 1; using these symbols as digits of a number, we can express any quantity.
Example : 1101.01
1 | 1 | 0 | 1 | . | 0 | 1
bit
binary point
Most Significant
Bit
Least Significant Bit

## Slide 12: Binary-to-Decimal Conversion
1 X 20 = 1
0 X 21 = 0
1 X 22 = 4
1 X 23 = 8
8 + 4 + 0 + 1 + 0 + 0.25 = 13.25
23 | 22 | 21 | 20 |  | 2-1 | 2-2
1 | 1 | 0 | 1 | . | 0 | 1
0 X 2-1 = 0
1 X 2-2 = 0.25

## Slide 13: Decimal-to-Binary Conversion (positional number)
125
250
2 5 0
2
2
Remainder 0
62
2
Remainder 1
31
2
Remainder 0
15
2
Remainder 1
7
2
Remainder 1
3
2
Remainder 1
1
Remainder 1
25010 = 1 1 1 1 1 0 1 02

## Slide 14: Hexadecimal System
The hexadecimal system is composed of 16 numerals or symbols.
These 16 symbols are
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, and F;
We can represent hexadecimal numbers in several ways
  10016 100h 100h 100H
  0x100
Decimal | Binary | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 15: Decimal/Hexadecimal Conversion
5 X 160 = 5
10 X 161 = 160
160 + 5 = 16510
161 | 160
A | 5
Hexadecimal to decimal
conversion
Decimal to Hexadecimal
conversion
250
16
15
Remainder 10
25010 = 15 1016 ?
= F A16

## Slide 16: Bits, Bytes, Nibbles, Word
Bit: a binary number digit
Byte: 8 bits
Nibble: half a byte (4 bits)
Word: depends on datapaths inside Computer, could be different width (4-bit, 8-bit, 16-bit, 32-bit)
  For example : ARM processor uses 32-bit internal datapath. Thus, WORD = 32 bits for ARM
MSB (Most Significant Byte) |  |  | LSB (Least Significant Byte)
0
7
8
15
16
23
24
31
Nibble
Byte
Word
Notes: Datapath = register + ALU

## Slide 17: Binary/Hexadecimal Conversion
Divide any size of binary numbers into nibbles
Represent each nibble as hexadecimal
Example : 1001011001011
I prefer binary, but it’s easy job for me to convert hex to binary
I prefer decimal but I can handle hex.
B
C
2
1
10010110010112 = 12CB16

## Slide 18: Representing Negative Numbers in Binary
Example:
510 – 710 = -210 How to represent in binary ?
There are 3 solutions:
  Signed-magnitude representation.
  1’s complement representation (reduced radix complement)
  2’s complement representation (radix complement)

## Slide 19: Solution 1: Signed-Magnitude
It’s the simplest representation for negative binary numbers.
In most computers, in order to represent both positive and negative numbers. The first bit (msb) is used as a sign bit.
  0 used for plus.
  1 used for minus.
Thus, for n-bit word, the first bit is the sign bit and n-1 bits represent the magnitude of the number.
1 0 0 0 0 0 0 0
Sign bit Magnitude

## Slide 20: Example: Signed Magnitude
Use signed-magnitude representation to represent these negative decimal numbers (8-bits)
-50
  50  50/2 = 25 remainder 0
  25/2 = 12 remainder 1
  12/2 = 6 remainder 0
  6/2 = 3 remainder 0
  3/2 = 1 remainder 1
  50  1 1 0 0 1 0
   0 1 1 0 0 1 0 ( add 0 to make magnitude 7 bits)
  -50  1 0 1 1 0 0 1 0 (add sign bit [1 for negative])

## Slide 21: Solution 2: 1’s Complement (1)
The 1’s complement of an N-digits binary integer B:
1’s complement = (2N – 1) – B
Example : Convert -510 to 4-bit 1’s complement
1’s complement = (24 – 1) – 5
= (16 – 1) – 5
= 1010  10102
-510 = 10102

## Slide 22: Solution 2: 1’s Complement (2)
Example : Convert -120 to a 8-bit 1’s complement representation
1’s complement = (28 – 1) – 120
= 256 – 1 – 120
= 13510  1000 01112
Let’s look again to simplify 1’s complement representation.
For 4-bits For 8-bits
  5  0101 120  01111000
  -5  1010 -120  10000111

## Slide 23: Solution 3: 2’s Complement (1)
Generating 2’s complement is more complex than other representations.
However, 2’s complement arithmetic is simpler than other arithmetic.
2’s complement = 2N – B , B ≠ 0
0 , B = 0

## Slide 24: Solution 3: 2’s Complement (2)
Example 1: Convert -510 to 4-bit 2’s complement
2’s complement = 24 – 5
= 16 – 5
= 1110  10112
-510 = 10112
Example 2: Convert -12010 to 8-bit 2’s complement representation
2’s complement = 28 – 120
= 256 – 120
= 136  1000 10002
-12010 = 100010002

## Slide 25: Solution 3: 2’s Complement (3)
Another method to calculate 2’s complement
  Convert number to 1’s complement
  Then, add 1 to that number
Example : Convert -12010 to 8-bit 2’s complement representation
12010 = 01111000
1’s complement  10000111 (invert bits)
2’s complement  10000111 + 1 = 100010002
-12010 = 100010002

## Slide 26: Solution 3: 2’s Complement (4)
Another method to calculate 2’s complement
  Keep same bit from LSB  MSB until found “1”
  Do 1’s complement on the rest bits.
Example : Convert -12010 to 8-bit 2’s complement representation
12010 = 01111000
= 10001000

## Slide 27: Representing Text in ASCII
In computer, textual information must be stored as binary numbers
Each character is represented as a 7-bit number known as ASCII code (American Standard Code for Information Interchange)
For example : ‘A’ is represented by 4116
b3 – b0
b6 – b4

## Slide 28: Assignment 1
Convert these binary system numbers to decimal system numbers
  0010 1101
  1111 1010
Convert these decimal system numbers to binary system numbers
  127
  38
Convert these numbers to binary system number
  5A16
  FAC016
Transform these decimal number to negative binary signed-magnitude, 1’s complement , and 2’s complement representation
(8-bits)
  -10, -98