## Slide 1: Introduction to Computer Architecture and System
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Objective
To understand
  What is the computer
  Von Neumann Architecture
  What is the microprocessors
  MU0 – Processor
  Instruction cycle
  Mnemonic and Machine Code

## Slide 3: What is the Computer
A computer is a programmable machine designed to sequentially and automatically carry out a sequence of arithmetic or logical operations. The particular sequence of operations can be changed readily, allowing the computer to solve more than one kind of problem.
The basic functions of the computer are :
  Inputting data
  Outputting data
  Processing data
  Storing data

## Slide 4: Computer Technology
Processor speed increases 2x every 18 months
Disk size increases 2x every year

## Slide 5: Unit of Measurement in Computer System
Normally, we use International System of Units (SI : Système international d'unités) as unit of measurement. But in computer system, we use binary prefix.
Name | Abbr | Factor | SI size
Kilo | K/k | 210 = 1,024 (K) | 103 = 1,000 (k)
Mega | M | 220 = 1,048,576 | 106 = 1,000,000
Giga | G | 230 = 1,073,741,824 | 109 = 1,000,000,000
Tera | T | 240 = 1,099,511,627,776 | 1012 = 1,000,000,000,000
Peta | P | 250 = 1,125,899,906,842,624 | 1015 = 1,000,000,000,000,000
Exa | E | 260 = 1,152,921,504,606,846,976 | 1018 = 1,000,000,000,000,000,000
Zetta | Z | 270 = 1,180,591,620,717,411,303,424 | 1021 = 1,000,000,000,000,000,000,000
Yotta | Y | 280 = 1,208,925,819,614,629,174,706,176 | 1024 = 1,000,000,000,000,000,000,000,000
For Example : A 400GB harddisk
Manufacturer uses GB in SI unit, so the harddisk has 400,000,000,000 B capacity
In MS Windows, it use GB as 230 , so the Windows can see the harddisk around 372 GB

## Slide 6: Von Neumann Architecture
The earliest computing machines had fixed programs. Changing the program of a fixed-program machine requires re-wiring, re-structuring, or re-designing the machine.
The idea of the stored-program computer changed all that: a computer that by design includes an instruction set and can store in memory a set of instructions (a program) that details the computation.
Characteristics of von Neumann machine
  Both data and instructions are stored in a read/write memory.
  Memory contents are addressable by location without regard for the type of data contained there
  Execution occurs in a sequential fashion by reading consecutive instructions from memory
John Von Neumann
1948 : You insist that there is something a machine cannot do.
If you will tell me precisely what it is that a machine cannot do,
then I can always make a machine which will do just that!

## Slide 7: Main Components of a Computer
Microprocessor
Main Memory
I/O Module
Instruction
Instruction
Instruction
Data
Data
Data
buffer
System bus

## Slide 8: What is the Microprocessor?
Microprocessor is a very large-scale integrated circuit (VLSI) that uses the architecture of the general-purpose digital computer.
Microprocessors are based on the von Neumann model of a stored program computer
The stored program computer, a microprocessor’s program is stored in memory along with its data

## Slide 9: MPU, MCU, CPU
Microprocessor Units (MPU) tend to be aimed at computer applications; they tend to have minimal "extras" on-chip.
  Intel Pentium
  AMD opteron
Microcontroller Units (MCU) tend to be aimed at embedded control applications; they tend to consist of a processor plus a number of useful peripherals (internal I/O modules, memory, etc).
  8051
  PIC
  ARM
Central Processing Unit (CPU) could refer to
  the actual processor part of a microcontroller.
  the microprocessor within a computer.

## Slide 10: Where are the CPU ?
Supercomputer
Personal computer
Mobile phone
High computing speed
Low computing speed
High power consumption
Low power consumption
Size : big
Size : small
Embedded Devices

## Slide 11: Embedded Devices

## Slide 12: Central Processing Unit (CPU)
Central Processing Unit (CPU) contains :
  ALU (Arithmetic Logic Unit)
    The ALU performs computational functions such as Add, Subtract, AND, OR, Compare, Increment, and Decrement.
  Control Logic
    The control logic decodes and executes the program. It also controls the memory, input, and output operation of the microprocessor
  Registers :
    The registers (fast memory, local to CPU) use to store temporary data and instructions

## Slide 13: Memory
The communication between microprocessor and memory has 3 types of signals (buses).
  Address bus – determines the location of memory
  Data bus – carries the contents of the location
  Control bus – governs the information transfer
The width of the address bus determines the size of memory. (how many location)
The width of the data bus determines the size of content. (how many bits can each location store)
Memory
Control bus
R/W
Enable
Address bus
A11:0
Data bus
D15:0

## Slide 14: Memory, Registers, and ALU
CPU
ALU
Registers
Memory
Address bus
A11:0
Address bus
A11:0
Data bus
D15:0
Data bus
D15:0
Control bus
Control bus

## Slide 15: MU0 – A Very Simple Processor
MU0 processor is an abstract design for teaching purposes at University of Manchester.
MU0 is a simple processor with 16-bits instruction and minimal hardware.
ALU
PC
ACC
IR
Memory
address bus
data bus
control
Program Counter (PC)
  Holds address of the next instruction to execute
Accumulator (ACC)
  Holds data being processed
Arithmetic Logic Unit (ALU)
  Performs operations on data
Instruction Register (IR)
  Holds current instruction code being executed

## Slide 16: Instructions
Instruction usually has 2 parts
  Opcode determines what is to be done
  Operand specifies where/what is the data
Opcode
Operand
1 word

## Slide 17: The Instruction Cycle
An instruction cycle is the basic operation cycle of a computer, sometimes called
  fetch-and-execute cycle
  fetch-decode-execute cycle
  FDX
Each computer's CPU can have different cycles based on different instruction sets, but will be similar to the following cycle:
  Fetch instruction – Supply instruction address and read an instruction from memory on the data bus.
  Decode instruction – Stored instruction is interpreted by CPU
  Fetch Operand – Supply address of data and read data into CPU
  Execution instruction - Perform the necessary action by CPU

## Slide 18: Step 1: Fetch Instruction (1)
CPU outputs value of program counter on address bus
Memory puts contents at the instruction address on the data bus
Instruction is stored in instruction register
ALU
PC
ACC
IR
Memory
address bus
data bus
control
IR

## Slide 19: Step 1: Fetch Instruction (2)
Program counter value is pushed onto the address bus
The ALU increment this value by k and put it back into Program counter
ALU
PC
ACC
IR
Memory
address bus
data bus
control
PC
PC = PC + k

## Slide 20: Step 2: Decode Instruction
The instruction word stored in IR is decoded by internal logic to provide control signals to ALU and other internal circuits inside CPU
ALU
PC
ACC
IR
Memory
address bus
data bus
control
IR

## Slide 21: Step 3: Fetch Operand
The instruction register provides the address of the data to be processed
Memory supplies the operand data on the data bus to the CPU, ready for processing either by the ALU or the ACC
ALU
PC
ACC
IR
Memory
address bus
data bus
control
IR

## Slide 22: Step 4: Execution Instruction
Processing is performed on the operand by the ALU according to the instruction
The result is put back into the Accumulator (ACC)
ALU
PC
ACC
IR
Memory
address bus
data bus
control
ACC

## Slide 23: MU0 – Instructions
Let us assume that the processor only has 8 instructions and can only access a maximum of 4k byte of memory. This implies that the address bus is only 12-bits wide
MU0 is a 16-bit microprocessor, Thus ALL instructions are 16-bits wide.
The 16-bit instruction code (machine code) has a format :
Top 4 bits define the operation code (opcode).
Next 12 bits define the memory address of the operand data.
Opcode
Operand
4 bits
12 bits

## Slide 24: MU0 – Instruction Set
2 load/store instructions: LDA, STO
2 computation instructions: ADD, SUB
4 control flow instructions: JMP, JGE, JNE, STP
Instruction (mnemonic) | Opcode | Effect
LDA S | 0000 | ACC := mem16[S]
STO S | 0001 | Mem16[S] := ACC
ADD S | 0010 | ACC := ACC + mem16[S]
SUB S | 0011 | ACC := ACC – mem16[S]
JMP S | 0100 | PC := S
JGE S | 0101 | If ACC >= 0, PC := S
JNE S | 0110 | If ACC != 0, PC := S
STP | 0111 | stop

## Slide 25: Example : First Program (1)
The simplest use of our microprocessor
  Add two numbers
    Let’s assume these numbers are stored at two consecutive locations in memory, with addresses 2E and 30
    Let’s assume we wish to store the result back to memory address 32
Hint : we need to load accumulator with 1 value, add the other, and then store the result back into memory

## Slide 26: Example : First Program (2)
Load accumulator with 1 value
  LDA 2E
Add the other
  ADD 30
Store the result back into memory
  STO 32
Stop program
  STP
Mnemonic | Machine code
LDA 2E | 0 02E
ADD 30 | 2 030
STO 32 | 1 032
STP | 7 000

## Slide 27: Example : How program works
MU0
ALU
Control
IR
ACC
PC
000
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus

## Slide 28: Example : Fetch-Decode Instruction
MU0
ALU
Control
IR
ACC
PC
000
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
002E

## Slide 29: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
PC
000
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
002E
ALU
PC
002

## Slide 30: Example : Fetch Operand
MU0
ALU
Control
ACC
PC
002
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
002E
ACC
00AA

## Slide 31: Example : Execution Instruction
MU0
ALU
Control
ACC
00AA
PC
002
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
002E

## Slide 32: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00AA
PC
002
002E
2030
1030
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
002E
IR
2030

## Slide 33: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00AA
PC
002
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
2030
ALU
PC
004

## Slide 34: Example : Fetch Operand
MU0
ALU
Control
ACC
00AA
PC
004
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
2030
ALU
0012

## Slide 35: Example : Execution Instruction
MU0
ALU
0012
Control
ACC
00AA
PC
004
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
2030
ALU
0012 + 00AA
ACC
00BC

## Slide 36: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00BC
PC
004
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
2030
IR
1032

## Slide 37: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00BC
PC
004
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
1032
ALU
PC
006

## Slide 38: Example : Execute Instruction
MU0
ALU
Control
ACC
00BC
PC
006
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
1032
00BC

## Slide 39: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00BC
PC
006
002E
2030
1032
7000
.
.
.
00AA
0012
00BC
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
1032
IR
7000

## Slide 40: Example : Fetch-Decode Instruction
MU0
ALU
Control
ACC
00BC
PC
006
002E
2030
1032
7000
.
.
.
00AA
0012
00BC
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
7000
ALU
PC
008

## Slide 41: Example : Execute Instruction
MU0
ALU
Control
ACC
00BC
PC
008
002E
2030
1032
7000
.
.
.
00AA
0012
000
002
004
006
02E
030
032
.
.
.
Address bus
Data bus
IR
7000
00BC
END

## Slide 42: Assignment 2
1. Write a program in mnemonic code for processor MU0 to calculate
A + B + C - D
where the value of
    A stores at address 2E0
    B stored at address 2E2
    C stored at address 2E4
    D stored at address 2E6
  The result will be store at address 2F0
2. Write the machine code for processor MU0 from the mnemonic code in question 1