## Slide 1: Introduction to the ARM processor
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Objective
To understand
  Computer Architecture
  Design Approaches : RISC and CISC
  Instruction Formats
  ARM Processor

## Slide 3: Computer Architecture
VLSI Circuit Design
Digital Design
Processor Architecture
I/O System
Application
Operating
System
Compiler
INSTRUCTION SET ARCHITECTURE
Level of
Abstraction
low
high
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine
Interpretation
x = y[i + 1];
x += 10;
LDA 02E
ADD 02F
ST0 030
0011 1001 1000 0010

## Slide 4: What is “Instruction Set Architecture (ISA)”
The attributes of [computing] system as seen by the programmer. i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation.
ISA includes :
  Organization of Programmable Storage
  Data Types and Data Structures: Encoding & Representation
  Instruction Formats
  Instruction (or Operation Code) Set
  Modes of Addressing and Accessing Data Items and Instructions
  Exceptional Conditions

## Slide 5: Instruction Set Architecture (ISA)
A very important abstraction
  Interface between hardware and low-level software
  Standardizes instructions, machine language bit patterns, etc.
  Advantage : different implementations of the same architecture
Modern instruction set architectures :
  80x86/Pentium/AMD
  PowerPC
  SPARC
  ARM ,etc.

## Slide 6: Processor Design Trade-Off
The art of processor design is to define an instruction set that supports the functions that are useful to the programmer whilst allowing an implementation that is as efficient as possible
Programmers generally want to express their program in as abstract a way as possible
Compiler is a bridge between high-level language and machine code
Thus, there are 2 design approaches :
  Complex Instruction Set Computers (CISC)
  Reduced Instruction Set Computers (RISC)

## Slide 7: Complex Instruction Set Computers (CISC)
Prior to 1980, the principal trend in instruction set design was towards increasing complexity in an attempt to help reducing the complexity of compiler.
Problem :
  Silicon die size
  Complexity in design
  Ex : PDP-11, VAX, Motorola 68k, x86

## Slide 8: Reduced Instruction Set Computers (RISC)
Simple instructions, fixed format
Pro:
  Smaller die size
  Shorter development time
  Ex : DEC Alpha, ARM, AVR, PowerPC, SPARC
  Ex : CISC FDX cycle
  Ex : RISC FDX cycle (pipelining)
F
D
E
F
D
E
F
D
E
F
D
E
F
D
E

## Slide 9: Review MU0-Processor
MU0 is a simple processor with 16-bits instruction and minimal hardware
MU0 Instruction format
12 bits Operand (12-bits address) means MU0 can access only 4k byte of memory
4 bits Opcode means MU0 can support only maximum16 instructions.
MU0 has few registers such as ACC, IR, PC.
Opcode
Operand
4 bits
12 bits

## Slide 10: How to improve MU0
Larger address space if we use 16-bit or 32-bit or wider address bus, we can access more memory.
Additional internal registers will be reduce the need for accessing external memory.
Addition addressing modes the way that the operand address maybe specified.
Each instruction uses as few clock cycles as possible
Make each clock cycle as short as possible (high clock rate)

## Slide 11: Instruction Formats
4-address instruction format
3-address instruction format (ARM processor)
2-address instruction format
1-address instruction format (MU0-processor)
Operand 1
f bits
n bits
Operand 2
Dest. Addr.
Next Inst. Addr.
Opcode
n bits
n bits
n bits
Operand 1
f bits
n bits
Operand 2
Dest. Addr.
Opcode
n bits
n bits
Operand 1
f bits
n bits
Dest. Addr.
Opcode
n bits
Operand 1
f bits
n bits
Opcode

## Slide 12: A First Look at the ARM Processor
Main features
  Load-store architecture
  Fixed-length (32-bit) instructions
  3-address instruction formats (2 sources operand registers, 1 result operand register)
  Conditional execution of ALL instructions
  Multiple Load-Store register instructions
  A single-cycle n-bit shift with ALU operation

## Slide 13: ARM’s application
ARM7TDMI-S (We will use in this class.)
  Game boy advanced
  Nintendo DS
  Apple Ipod
  Garmin, ..etc..
ARM1176JZ(F)-S
  Iphone 3G, Nintendo 3DS
Cortex-A8
  HTC Desire, iPhone 3GS, iPhone 4, iPad, Samsung Galaxy S, Samsung Galaxy Tab
Cortex-A9
  Samsung Galaxy S II, iPad 2, iPhone 4S, LG Optimus 2X, Asus Eee Pad Transformer

## Slide 14: Visible Registers
R0 – R14 are general purpose registers (32-bits)
R15 is the program counter
Current Program Status Register (CPSR) contains conditional flags and other status bits

## Slide 15: ASSEMBLY Language Programming
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka

## Slide 16: ARM Assembly Language Programming
The following is a simple example which illustrates some of the core constituents of an ARM assembler module:
Comment
Operands
Opcode
Label

## Slide 17: General Layout of an Assembly Program
To general form of lines in an assembler module is
Label Opcode Operands ; Comment
Each field must be separated by one or more “whitespace” (such as a space or a tab)
Actual instructions never start in the first column, since they must be preceded by whitespace, even if there is no label.
Example

## Slide 18: AREA, ENTRY, END Directives
Directives are instruction to the assembler program, NOT to the microprocessors
AREA Directive – specifies chunks of data or code that are manipulated by the linker
ENTRY Directive – marks the first instruction to be executed within an application
END Directive – markes the end of the module

## Slide 19: Basic instructions (1)
MOV register1, register2
  register1  register2
  Example :
    MOV r0, r1 ; r0  r1
    MOV r2, r3 ; r2  r3
MOV register, immediate_number
  register1  immediate_number
  ** For now, immediate number must fit in 8 bits **
  Example :
    MOV r0, #100 ; r0  10010
    MOV r1, #0x20 ; r1  2016

## Slide 20: Basic instructions (1)
ADD register1, register2, register3
  register1  register2 + register3
  Example :
    ADD r0, r1, r2 ; r0  r1 + r2
    ADD r5, r3, r0 ; r5  r3 + r0
SUB register1, register2, register3
  register1  register2 – register3
  Example :
    SUB r0, r1, r2 ; r0  r1 - r2
    SUB r5, r3, r0 ; r5  r3 - r0

## Slide 21: Example
AREA FirstExample, CODE, READONLY
ENTRY
start
MOV r0, #10
MOV r1, #0x20
ADD r2, r1, r0
SUB r3, r1, r0
END
0x00 00 00 00
0x00 00 00 00
0x00 00 00 00
0x00 00 00 00
0x00 00 00 00
R15 (PC)
R0
R1
R2
R3
0x00 00 00 04
0x00 00 00 0A
0x00 00 00 08
0x00 00 00 20
0x00 00 00 0C
0x00 00 00 2A
0x00 00 00 16
0x00 00 00 10

## Slide 22: Assignment 3
Given the following code
    AREA assignment, CODE, READONLY
    ENTRY
    MOV r0, #12
    MOV r1, #15
    MOV r2, r1
    ADD r2, r0, r2
    SUB r2, r2, r0
    END
What are the data contains in r0, r1, r2 and PC registers ? (answer in hexadecimal system)
Write a program in assembly to compute the following equation
Result = (5 + 3 + 10) – 4
by using only 2 registers (r0 and r1), the result stores at r0 register.