## Slide 1: Condition code and Arithmetic Operations
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Objectives
To understand
  Overflow and Underflow
  CPSR condition flags
  Arithmetic Operation Instructions

## Slide 3: Review : Binary Addition/Subtraction
Binary number
  1001 + 1100 ?
  1100 - 0010 ?
In 4-bit microprocessor (2’s complement)
  1001 + 1100 ?
  1100 - 0010 ?

## Slide 4: Overflow and Underflow
Overflow occurs when an arithmetic operation yields a result that is greater than the range’s positive limit of 2N-1 – 1
Underflow occurs when an arithmetic operation yields a result that is less than the range’s negative limit of -2N-1

## Slide 5: Example : overflow
510 + 610 (4-bits 2’s complement)
Note that 4 bits can store +7 to -8
5 0101
+ 6 + 0110
1110 1011  -510
11 ≠ -5 OVERFLOW

## Slide 6: Example : underflow
-510 - 710 (4-bits 2’s complement)
Note that 4 bits can store +7 to -8
-5 1011
+ -7 + 1001
-1210 1 0100  410
-12 ≠ 4 UNDERFLOW

## Slide 7: Status Flags in Program Status Register CPSR
N = Negative result from ALU flag
Z = Zero result from ALU flag
C = ALU opertion Carried out
V = ALU operation oVerflowed
Flags | Arithmetic Instruction
Negative (N = ‘1’) | Bit 31 of the result has been set indicates a negative number in signed operation
Zero (Z = ‘1’) | Result of operation was zero
Carry (C = ‘1’) | Result was greater than 32 bits
Overflow (V = ‘1’) | Result was greater than 32 bits indicates a possible corruption of the sign bit in signed number

## Slide 8: Experimentation with Condition Flags (1)
Assume 4 bit-number 0011 + 0010
0 0 1 1 +
0 0 1 0
1
0
1
1
0
0
0
0
0
Negative (N) = ?
Zero (Z) = ?
Carry (C) = ?
Overflow (V) = ?
0
0
0
0
Overflow (V) =
MSB carry in XOR MSB carry out

## Slide 9: Experimentation with Condition Flags (2)
Assume 4 bit-number 1111 + 0010
1 1 1 1 +
0 0 1 0
1
0
0
1
0
0
1
1
1
Negative (N) = ?
Zero (Z) = ?
Carry (C) = ?
Overflow (V) = ?
0
0
1
0
Why V is 0 ?

## Slide 10: Experimentation with Condition Flags (3)
Assume 4 bit-number 0111 + 0010
0 1 1 1 +
0 0 1 0
1
1
0
1
0
0
1
0
0
Negative (N) = ?
Zero (Z) = ?
Carry (C) = ?
Overflow (V) = ?
Notes: N = 1, Z = 0, C = 0, V = 1

## Slide 11: Experimentation with Condition Flags (4)
Assume 4 bit-number 1110 + 1001
1 1 1 0 +
1 0 0 1
1
0
1
0
1
0
0
1
1
Negative (N) = ?
Zero (Z) = ?
Carry (C) = ?
Overflow (V) = ?
Notes: N = 0, Z = 0, C = 1, V = 1

## Slide 12: Exercise : Condition Flags
Assume 4 bit-number, What are the values store in condition flags (N, Z, C, V) of the following operations.
  1001 + 1010
  1011 + 0101
  1110 – 0111
  0110 – 0010
Notes: N = 1, Z = 0, C = 1, V = 1
N

## Slide 13: More on ARM Assembly Instructions
Largest category of ARM instructions, all sharing the same instruction format
Load/Store architecture
  These instructions only work on registers, NOT memory
They each perform a specific operation on operands
  4 fields format : 1, 2, 3, 4
    Operation by name
    Operand getting result (“destination”)
    1st operand for operation (“source 1”)
    2nd operand for operation : register or shifted register or immediate (numerical constant)

## Slide 14: Review : Instructions we’ve learnt
4 fields format : 1, 2, 3, 4
  Operation by name
  Operand getting result (“destination”)
  1st operand for operation (“source 1”)
  2nd operand for operation : register or shifted register or immediate (numerical constant)
1 | 2 | 3 | 4
ADD | R0, | R1, | R2
ADD | R0, | R1, | #100
ADD | R0, | R1, | #0x20

## Slide 15: Review: Registers
ARM processor has register R0 – R15
By convention, each register also has a name to make it easier to code
Register Number | Register Name
R0 | a1
R1 | a2
R2 | a3
R3 | a4
R4 | v1
R5 | v2
R6 | v3
R7 | v4
R8 | v5
R9 | v6
R10 | v7
R11 | v8
Register Number | Register Name
R12 | IP
R13 | SP
R14 | LR
R15 | PC
IP : Intra Procedure-call scratch register
SP : Stack Pointer
LR : Link Register
PC : Program Counter
ADD R0, R1, R2 = ADD a1, a2, a3
MOV R0, R15 = MOV a1, PC

## Slide 16: Arithmetic Operations
ADD reg1, reg2, reg3 ;reg1  reg2 + reg3
ADC reg1, reg2, reg3 ;reg1  reg2 + reg3 + C
SUB reg1, reg2, reg3 ;reg1  reg2 - reg3
SBC reg1, reg2, reg3 ;reg1  reg2 - reg3 + C – 1
RSB reg1, reg2, reg3 ;reg1  reg3 - reg2
RSC reg1, reg2, reg3 ;reg1  reg3 - reg2 + C – 1
** C = Carry bit in the CPSR **

## Slide 17: Example 1
AREA ex1, CODE, READONLY
ENTRY
start
MOV a1, #0x5
MOV a2, #0x1A
RSB a3, a1, a2
END
After the execution of the program is terminated,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR

## Slide 18: Example 2
AREA ex2, CODE, READONLY
ENTRY
start
MOV a1, #0x0
MOV a2, #0x0
ADC a3, a1, a2
END
After the execution of the program is terminated,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR

## Slide 19: Updating Condition Flags in CPSR
Normally, data processing instructions such as ADD, ADC, SUB, etc. do not change the value of condition flags in CPSR
We can add S at the end of instructions to indicate that the condition code (flag) should be updated
Instruction (not update CC) | Instruction (update CC)
ADD | ADDS
ADC | ADCS
SUB | SUBS
SBC | SBCS
RSB | RSBS
RSC | RSCS

## Slide 20: Example 3
AREA ex3, CODE, READONLY
ENTRY
start
MOV a1, #0x0
MOV a2, #0x0
ADCS a3, a1, a2
END
After the execution of the program is terminated,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR

## Slide 21: Example 4
AREA ex4, CODE, READONLY
ENTRY
start
MOV a1, #0xFFFFFFFB
MOV a2, #0x5
ADDS a3, a1, a2
END
After the execution of the program is terminated,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR

## Slide 22: Example 5
AREA ex4, CODE, READONLY
ENTRY
start
MOV a1, #0xFFFFFFFB
MOV a2, #0x5
ADDS a3, a1, a2
ADD a3, a1, a2
END
After the execution of the program is terminated,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR

## Slide 23: Assignment 4
AREA assignment4, CODE, READONLY
ENTRY
start
MOV a1, #0xFFFFFF00
MOV a2, #0xFFFFFF58
ADDS a3, a1, a2
MOV a2, #0x1B
RSCS a3, a2, a3
END
Assume 8 bit-number, What are the values store in condition flags (N, Z, C, V) of the following operations
  0xCA + 0x17
  0xF0 + 0xF8
  0x6F - 0x75
  0xC5 - 0xD6
After the execution of the program is terminated in ARM processor,
  What are the value store in r0, r1, and r2
  What are the value in N, Z, C, V bit of CSPR