## Slide 1: Multiplication
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Review : ARM Instruction so far
ADD : Addition
SUB : Subtraction
MOV : Move
AND : And
BIC : And not
ORR : Or
EOR : Xor
LSL : Shift left
LSR : Shift right
ASR : Arithmetic Shift Right
ROR : Rotate right

## Slide 3: Decimal Multiplication
In decimal
  Multiplying by 10 is same as shifting left by 1
    54 * 10 = 540
    120 * 10 = 1200
  Multiplying by 100 is same as shifting left by 2
    54 * 100 = 5400
    120 * 100 = 12000
  Multiplying by 10n is same as shifting left by n

## Slide 4: Binary Multiplication
In Binary
  Multiplying by 2 (102) is same as shifting left by 1
    112 * 102 = 1102
    1012 * 102 = 10102
  Multiplying by 4 (1002) is same as shifting left by 2
    112 * 1002 = 11002
    1012 * 1002 = 101002
  Multiplying by 2n is same as shifting left by n

## Slide 5: Multiply by Power of 2 via Shift Left
Since shifting is so much faster than the multiplication
A good compiler usually notice for example C code multiplies by power of 2 and compiles it to a shift instruction
Example
  In C: A = A * 8
  In Assembly : MOV R0, R0, LSL #3

## Slide 6: Shift, Add and Subtract for Multiplication
In Depth techniques :
Example 1 :
  In C : R0 = 5 * R1
  In ARM Assembly:
    R0 = (4 + 1) * R1
    = (4 * R1) + R1 = R1 + (4 * R1)
    ADD R0, R1, R1, LSL #2
Example 2 :
  In C : R0 = 105 * R1
  In ARM Assembly :
    R0 = (15 * 7) * R1
    = (16 – 1) * (8 - 1) * R1
    RSB R0, R1, R1, LSL #4 ; (16 – 1) * R1
    RSB R0, R0, R0, LSL #3 ; (8 – 1) * R0

## Slide 7: Multiply (unsigned) : Example
Multiplicand (810) 1 0 0 0
Multiplier (910) 1 0 0 1
X
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
1
0
0
1
m bits x n bits = m + n bit product
Thus, 32 bits X 32 bits = 64 bits value
=7210

## Slide 8: Multiply (signed) : Example
Multiplicand (-810) 1 0 0 0
Multiplier (-710) 1 0 0 1
X
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
1
0
0
1
= 7210
0

## Slide 9: 2’s Complement Multiplication
A sequence of 2’s complement addition except for last step, we do the subtraction.
Multiplicand (-810) 1 0 0 0
Multiplier (-710) 1 0 0 1
X
0
0
0
1
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
0
0
0
1
0
2’s complement..
0
0
0
1
1
1
0
0
1
=5610

## Slide 10: 2’s Complement Multiplication (more example)
Multiplicand (-810) 1 0 0 0
Multiplier ( 310) 0 0 1 1
X
0
0
0
1
1
1
1
1
0
0
0
1
1
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
2’s complement..
0
0
0
1
0
1
1
1
1
=2410
2’s complement..
0
0
0
1
1
0
0
0

## Slide 11: Multiplication Instructions
BASIC ARM Multiplication
  MUL Rd, Rm, Rs ; Rd = Rm * Rs ;signed [31:0]
  Warning : Rd can’t be the same as Rm
Multiply-Long
  UMULL RdHi, RdLo, Rm, Rs ;unsigned
  SMULL RdHi, RdLo, Rm, Rs ;signed
    RdHi = Rm * Rs [63:32]
    RdLo = Rm * Rs [31:0]
** No Division Instruction in ARM **
  Division has to be done in software through a sequence of shift/subtract/add instruction (too much for this class)

## Slide 12: Exercise 1
Given
  R2 stores value -10
  R3 stores value 2
After execute the instruction
  SMULL R0, R1, R2, R3
What is the value stores in R0 and R1 ?

## Slide 13: Memory Access
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka

## Slide 14: ARM and Memory
Up until now, we learnt the ARM instructions
  ADD, SUB, LSL, LSR, ORR, XOR, MOV, ..etc.
Remember ?, ARM arithmetic instructions only operate on registers, never directly on memory.
Data Transfer Instructions transfer data between registers and memory:
  Memory to Register
  Register to Memory

## Slide 15: Review : MOV with Immediate
MOV R0, #12
  Immediate value must be fit in 8 bit
  Immediate value can get by rotate even number of bit
    MOV R0, #0xFF000000 ; 0xFF rotate right by 24 bit
  MOV R0, #0x123456 doesn’t work !!
LDR R0, =0x123456
  Assembler will allocate memory and store value 0x123456 for you, then LDR instruction will load value from that address to the register
Why not always use LDR instruction for immediate value ?
  Loading value from memory is much SLOWER than generating it by ALU.

## Slide 16: Data Transfer : Memory to Register (1)
To transfer a word of data, we need to specify two things :
  Register
  Memory Address
Think of memory as a single one-dimension array, so we can address it simply by supplying a pointer to a memory address
Other times, we want to be able to offset from this pointer
0x40000000
0x40000004
0x40000008
0x4000000C
0x40000010
pointer
offset

## Slide 17: Data Transfer : Memory to Register (2)
To specify a memory address to copy from, specify two things :
  A register which contains a pointer to memory
  A numerical offset (in bytes), or a register which contain an offset
The desired memory address is the sum of these two values
Example 1: [ v1 , #8 ]
  Specifies the memory address pointed by the value in v1 + 8 bytes
Example 2: [ v1, v2 ]
  Specifies the memory address pointed by the value in v1 + v2

## Slide 18: Data Transfer : Memory to Register (3)
Load Instruction Syntax :
  LDR 1, [ 2, 3 ]
    1 : register that will receive value
    2 : register containing pointer to memory
    3 : numerical offset in bytes or
    another shifted index register
Example
  LDR R0, [ R1, #8]
  LDR R0, [ R1, R2]
Base register
Offset
Index register

## Slide 19: Example 1
Given a table of memory address and its stored data, What the value in R0, R1, and R2 after executing the programs
Value | Address
0x10 | 0x4000 0000
0x20 | 0x4000 0004
0x30 | 0x4000 0008
0x50 | 0x4000 000C
0x10 | 0x4000 0010
0x45 | 0x4000 0014
0xFF | 0x4000 0018
AREA ex1, CODE, READONLY
ENTRY
start
LDR R2, =0x40000000
MOV R3, #4
LDR R0, [R2, R3]
LDR R1, [R2, #16]
END

## Slide 20: Pre Indexed Load Instruction
Pre Indexed Load Instruction Syntax :
  LDR 1, [ 2, 3]!
    1 : register that will receive value
    2 : register containing pointer to memory
    3 : numerical offset in bytes or
    another shifted index register
This instruction will take 2 step
  1) Register “1” loads the value from the memory pointed by the pointer in “2”, add “3” bytes
  2) “2” is updated by computed sum of “2” and “3”
Example : Let R1 = 0x4000 0000
  LDR R0, [R1, #0x12] !
    Load R0  mem[ R1 + 0x12 ] ; R0  mem [0x4000 0012]
    Update base register : R1  R1 + 0x12 ; now R1 = 0x4000 0012

## Slide 21: Example 2
Given a table of memory address and its stored data, What the value in R0, R1, R2 after execution the programs
Value | Address
0x10 | 0x4000 0000
0x20 | 0x4000 0004
0x30 | 0x4000 0008
0x50 | 0x4000 000C
0x10 | 0x4000 0010
0x45 | 0x4000 0014
0xFF | 0x4000 0018
AREA ex2, CODE, READONLY
ENTRY
start
LDR R2, =0x40000000
MOV R3, #4
LDR R0, [R2, R3] !
LDR R1, [R2, #16] !
END

## Slide 22: Post Indexed Load Instruction
Post Indexed Load Instruction Syntax :
  LDR 1, [ 2 ] , 3
    1 : register that will receive value
    2 : register containing pointer to memory
    3 : numerical offset in bytes or
    another shifted index register
This instruction will take 2 step
  1) Register “1” loads the value from the memory pointed by the pointer in “2”
  2) “2” is updated by computed sum of “2” and “3”
Example : Let R1 = 0x4000 0000
  LDR R0, [ R1 ], #0x12
    Load R0  mem[ R1] ; R0  mem [0x4000 0000]
    Update base register : R1  R1 + 0x12 ; now R1 = 0x4000 0012

## Slide 23: Example 3
Given a table of memory address and its stored data, What the value in R0, R1 and R2 after execution the programs
Value | Address
0x10 | 0x4000 0000
0x20 | 0x4000 0004
0x30 | 0x4000 0008
0x50 | 0x4000 000C
0x10 | 0x4000 0010
0x45 | 0x4000 0014
0xFF | 0x4000 0018
AREA ex3, CODE, READONLY
ENTRY
start
LDR R2, =0x40000000
MOV R3, #4
LDR R0, [R2], R3
LDR R1, [R2], #16
END

## Slide 24: Data Transfer : Register to Memory
For storing data in register to memory, we will use STR instruction
STR instruction syntax is identical to LDR instruction syntax
STR : store from register, so 32 bits or one word are stored from register to memory at a time
Example : Let R1 = 0x4000 0000, R2 = 0x8
  STR R0, [R1, #0x12]
    Store R0  mem[ R1 + 0x12 ] ; R0  mem [0x4000 0012]
  STR R0, [R1, R2]
    Store R0  mem[ R1 + R2] ; R0  mem [0x4000 0008]

## Slide 25: Pre Indexed Store Instruction
Pre Indexed Store Instruction Syntax :
  STR 1, [ 2, 3]!
    1 : register that will send value
    2 : register containing pointer to memory
    3 : numerical offset in bytes or
    another shifted index register
This instruction will take 2 step
  1) Register “1” stores the value to the memory pointed by the pointer in “2”, add “3” bytes
  2) “2” is updated by computed sum of “2” and “3”
Example : Let R1 = 0x4000 0000
  STR R0, [R1, #0x12] !
    Store R0  mem[ R1 + 0x12 ] ; R0  mem [0x4000 0012]
    Update base register : R1  R1 + 0x12 ; now R1 = 0x4000 0012

## Slide 26: Post Indexed Store Instruction
Post Indexed Store Instruction Syntax :
  STR 1, [ 2 ] , 3
    1 : register that will send value
    2 : register containing pointer to memory
    3 : numerical offset in bytes or
    another shifted index register
This instruction will take 2 step
  1) Register “1” stores the value to the memory pointed by the pointer in “2”
  2) “2” is updated by computed sum of “2” and “3”
Example : Let R1 = 0x4000 0000
  STR R0, [ R1 ], #0x12
    Store R0  mem[ R1] ; R0  mem [0x4000 0000]
    Update base register : R1  R1 + 0x12 ; now R1 = 0x4000 0012

## Slide 27: Example 4
Complete the values in the given table of memory address and its stored data after execution the programs
Value | Address
0 | 0x4000 0000
0 | 0x4000 0004
0 | 0x4000 0008
0 | 0x4000 000C
0 | 0x4000 0010
0 | 0x4000 0014
AREA ex4, CODE, READONLY
ENTRY
start
MOV R0, #0xFF
LDR R2, =0x40000000
MOV R3, #8
STR R0, [R2, R3]
STR R0, [R2], R3
STR R0, [R2, R3] !
END

## Slide 28: ARM : Memory Map
CODE (ROM)
ON-CHIP RAM
We can work with Local on-chip memory from address 0x4000 0000
to address 0x4000 FFFFF

## Slide 29: Memory Alignment
Don’t forget that sequential word addresses in ARM with byte addressing do not differ by 1
ARM requires that all words start at addresses that are multiples of 4 bytes
3 | 2 | 1 | 0
Aligned
Not
Aligned

## Slide 30: Assignment 6
Solve the following expression in 4-bits register step-by-step
  -5 x -2
  5 x -2
Complete the value in memory table after program is executed
Value | Address
? | 0x4000 0000
? | 0x4000 0004
? | 0x4000 0008
? | 0x4000 000C
? | 0x4000 0010
AREA hw6, CODE, READONLY
ENTRY
start
MOV R1, #1
LDR R2, =0x40000000
MOV R3, #4
STR R1, [R2, R3]!
LSL R1, #2
STR R1, [R2, R3]!
LSL R1, #2
STR R1, [R2, R3]!
LDR R2, =0x40000000
LDR R0, [R2, #8 ]!
LDR R1, [R2] , #4
ADD R0, R0, R1, LSL #4
STR R0, [R2, #4]
END