## Slide 1: Making Decision
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Review: C Decision (Control Flow)
2 kinds of if statement in C
  if (condition) statement
  if (condition) statement1 else statement2
Example 1:
if ( a == 5 ) printf(“Hello”);
Example 2 :
  if ( a == 5 ) printf(“Hello”);
  else printf(“Hi”);

## Slide 3: Using Goto and Label
C syntax :
  if ( a == 5 ) printf(“Hello”);
  else printf(“Hi”);
Goto and Label syntax :
if ( a == 5) goto Label1;
printf(“Hi”);
goto Label2;
Label1:
printf(“Hello”);
Label2:
a = 5 ?
printf(“Hello”)
printf(“Hi”)
true
false

## Slide 4: ARM Decision Instructions (Control Flow)
Decision Instruction in ARM
  CMP register1, operand2 ;compare register1 with operand 2
  BEQ Label ; branch to Label if equal
  BNE Label ; branch to Label if not equal
  B Label ; branch to Label
C Code
if ( a == 5) goto Label1;
a = a + 5;
goto Label2;
Label1:
a = a - 5;
Label2:
ARM Code (a maps to R0)
CMP R0, #5 ;if (a == 5)
BEQ Label1 ; goto Label1
ADD R0, R0, #5 ;a = a + 5
B Label2 ; goto Label2
Label1 SUB R0, R0, #5 ; a = a - 5
Label2

## Slide 5: Example 1
Convert the following C program to ARM assembly. Assume that a maps to R0, and b maps to R1
if ( a != 5 )
{
b = a + 5;
a = a - 2;
}
a = a + b;
Do if condition
is true
Do always
Transform to
goto-label
if ( a == 5 ) goto Endif
b = a + 5;
a = a - 2;
Endif: a = a + b;
Transform to ARM assembly
CMP R0, #5
BEQ Endif
ADD R1, R0, #5
SUB R0, R0, #2
Endif ADD R0, R0, R1

## Slide 6: Exercise 1
Convert the following C program to ARM assembly. Assume that a maps to R0, and b maps to R1
if ( a != 10)
{
b = a + 10;
a = a - 5;
}
else {
b = a + 20;
a = a – 10;
}
a = a + b;
Do if condition is
true
Do if condition is
false
Do always

## Slide 7: Simple Loop (1)
Simple loop in C (goto-label)
Loop: i = i + 1; if (i != 5) goto Loop;
ARM Assembly (i maps to R0)
Loop ADD R0, R0, #1
CMP R0, #5 BNE Loop
i != 5 ?
i = i + 1
true
false

## Slide 8: Simple Loop (2)
In C, normally we use while or for instead of goto-label
while( i != 10)
i = i + 1;
ARM Assembly (i maps to R0)
Loop CMP R0, #10
BEQ EndLoop ADD R0, R0, #1
B Loop
EndLoop
i != 10 ?
i = i + 1
true
false

## Slide 9: More on Branch Instructions
So far, we branch on Uncondition, Equal, and Not Equal (B, BEQ, and BNE)
How about
  Greater than >
  Greater than or equal >=
  Less than <
  Less than or equal <=
Lucky for us, ARM has these instructions for you.
  BGT (Branch greater than)
  BGE (Branch greater than or equal)
  BLT (Branch less than)
  BLE (Branch less than or equal)

## Slide 10: Example 2
Convert the following C program to ARM assembly. Assume that a maps to R0, and b maps to R1
while (a < 5) {
a = a + 1;
b = b + 2;
}
Transform to
goto-label
WhileLoop:
if ( a >= 5 ) goto EndWhile
a = a + 1;
b = b + 2;
goto WhileLoop
EndWhile:
Transform to ARM assembly
WhileLoop CMP R0, #5
BGE EndWhile
ADD R0, R0, #1
ADD R1, R1, #2
B WhileLoop
EndWhile

## Slide 11: Exercise 2
Convert the following C program to ARM assembly. Assume that a maps to R0, and b maps to R1
while ( a <= 10)
{
b = a + 10;
a = a - 5;
}
a = a + b;

## Slide 12: If- else if - else
In ARM : (R0 = k, R1 = a)
CMP R0, #1
BNE Cond2
ADD R1, R1, #5
B Endif
Cond2 CMP R0, #2
BNE Cond3
ADD R1, R1, #10
B Endif
Cond3 CMP R0, #3
BNE ElseCond
SUB R1, R1, #10
B Endif
ElseCond SUB R1, R1, #5
Endif
In C : if – else if - else
if (k == 1) a = a + 5;
else if (k == 2) a = a + 10;
else if (k == 3) a = a - 10;
else a = a – 5;
What is the a value after program is executed if assume a = 20 and
k = 1
k = 2
k = 3
k = 10

## Slide 13: Comparing unsigned data
Up until now, BGT, BGE, BLT, and BLE use to compare signed data NOT unsigned data.
Example (8-bit register)
  A1 = 0xF5 , A2 = 0x05
  So A1 > A2 or A2 > A1 ??
  Signed : A1 = -1110, A2 = 510 (A2 > A1)
  Unsigned : A1 = 24510, A2 = 510 (A1 > A2)
In ARM, there are instruction for comparing and branching unsigned data
  BLO Branch Lower (unsigned)
  BLS Branch Less or Same (unsigned)
  BHI Branch Higher (unsigned)
  BHS Branch Higher or Same (Unsigned)

## Slide 14: Example 3
What is the value in R2 after program is executed ?
LDR R0, =0xFFFF5011
LDR R1, =0x000ABCD
MOV R2, #5
CMP R0, R1
BGE Exit
ADD R2, R2, #1
Exit
LDR R0, =0xFFFF5011
LDR R1, =0x000ABCD
MOV R2, #5
CMP R0, R1
BHS Exit
ADD R2, R2, #1
Exit
(1)
(2)

## Slide 15: How can branch instruction know the output of CMP instruction ?
In the process of comparison and branching (CMP), actually, processor does the following steps :
  CMP instruction does operand1 – operand2
  Update CPSR flags
  Branch instruction checks CPSR flags and does the operation
Review : CPSR

## Slide 16: CMP and CSPR (=)
CMP R0, R1 ; it does R0 – R1
  R0 = R1 (R0 = 0x15, R1 = 0x15)
  0 0 0 1 0 1 0 1 +
  1 1 1 0 1 0 1 1
  0 0 0 0 0 0 0 0
  N = 0, Z = 1, C = 1, V = 0
  Thus, if R0 = R1 then Z = 1

## Slide 17: CMP and CSPR (!=)
CMP R0, R1 ; it does R0 – R1
  R0 != R1 (R0 = 0x15, R1 = 0x10)
  0 0 0 1 0 1 0 1 +
  1 1 1 1 0 0 0 0
  0 0 0 0 0 1 0 1
  N = 0, Z = 0, C = 1, V = 0
  Thus, if R0 != R1 then Z = 0

## Slide 18: CMP and CSPR (unsigned data >=)
CMP R0, R1 ; it does R0 – R1
  R0 >= R1 (R0 is higher than or same as R1)
    R0 = 0xF0, R1=0x05
    1 1 1 1 0 0 0 0 +
    1 1 1 1 1 0 1 1
    1 0 0 0 0 1 0 1 1
    R0 = 0x06, R1 = 0x05
    0 0 0 0 0 1 1 0 +
    1 1 1 1 1 0 1 1
    1 0 0 0 0 0 0 0 1
    N = ?, Z = 0, C = 1, V = 0

## Slide 19: CMP and CSPR (unsigned data <)
CMP R0, R1 ; it does R0 – R1
  R0 < R1 (R0 is lower than R1)
    R0 = 0x05, R1=0xF0
    0 0 0 0 0 1 0 1 +
    0 0 0 1 0 0 0 0
    0 0 0 1 0 1 1 1
    R0 = 0x05, R1 = 0x06
    0 0 0 0 0 1 0 1 +
    1 1 1 1 1 0 1 0
    1 1 1 1 1 1 1 1
    N = ?, Z = 0, C = 0, V = 0

## Slide 20: Conclusion : CPSR Flags for CMP Unsigned Data
N | Z | C | V | Remark
X | 1 | X | X | R0 = R1
X | 0 | X | X | R0 != R1
X | X | 1 | X | R0 >= R1 (higher or same)
X | X | 0 | X | R0 < R1 (lower)
CMP R0, R1
X X | 1 X | X 0 | X X | R0 <= R1 (lower or same) R0 = R1 OR R0 < R1
X | 0 | 1 | X | R0 > R1 (higher) R0 != R1 AND R0 >= R1

## Slide 21: CMP and CSPR (signed data >=)
CMP R0, R1 ; it does R0 – R1
  R0 >= R1 (R0 is greater than or equals R1)
    R0 – R1 (always positive N = 0, V = 0)
    Exceptional case : when result of subtraction is overflow
    R0 = 0x75, R1=0x85
    0 1 1 1 0 1 0 1 +
    0 1 1 1 1 0 1 1
    0 1 1 1 1 0 0 0 0
    Carry In (1) XOR Carry Out (0) => V = 1
    N = 1
  Thus, if N = V then R0 is greater than or equals to R1

## Slide 22: CMP and CSPR (signed data <)
CMP R0, R1 ; it does R0 – R1
  R0 < R1 (R0 is less than R1)
    R0 – R1 (always negative N = 1, V = 0)
    Exceptional case : when result of subtraction is overflow
    R0 = 0x85, R1=0x75
    1 0 0 0 0 1 0 1 +
    1 0 0 0 1 0 1 1
    1 0 0 0 1 0 0 0 0
    Carry In (0) XOR Carry Out (1) => V = 1
    N = 0
  Thus, if N != V then R0 is greater than or equals to R1

## Slide 23: Conclusion : CPSR Flags for CMP Signed Data
N | Z | C | V | Remark
X | 1 | X | X | R0 = R1
X | 0 | X | X | R0 != R1
0 1 | X X | X X | 0 1 | R0 >= R1 (greater than or equal)
1 0 | X X | X X | 0 1 | R0 < R1 (less than)
CMP R0, R1
X 1 0 | 1 X X | X X X | X 0 1 | R0 <= R1 (less than or equal) R0 = R1 OR R0 < R1
0 1 | 0 0 | X X | 0 1 | R0 > R1 (greater than) R0 != R1 AND R0 >= R1

## Slide 24: Flag Setting Instructions
Compare
  CMP R0, R1 ;update flags after R0 – R1
Compare Negated
  CMN R0, R1 ;update flags after R0 + R1
Test
  TST R0, R1 ;update flags after R1 AND R2
Test Equivalence
  TEQ R0, R1 ;update flags after R1 EOR R2

## Slide 25: Assignment 7
Convert the following part of C program to ARM Assembly
int a = 0, b = 0;
while ( b <= 10)
{
if ( a < 5)
a = a + 10;
else
a = a - 5;
b = b + 1;
}
a = a + b;
b <= 10 ?
a = a + b
true
false
a = 0, b = 0
a < 5 ?
a = a + 10
a = a - 5
true
false
b = b + 1