## Slide 1: OUTPUT Interface
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: ARM Memory Structure
AHB = Advanced High-Performance Bus
  Start at memory address 0xF000 0000
APB = Advanced Peripheral Bus
  Start at memory address 0xE000 0000
Memory access also reading/ writing a sequence of bytes, so use loads for input, stores for output
  Called “Memory Mapped Input/Output”
  A portion of the address space dedicated to communication paths to Input or Output devices (no memory there)

## Slide 3: GPIO
GPIO (General Purpose Input/Output)
We can use GPIO as an Input or an Output port
  Input : input digital/analog signal to Microprocessor
  Output : digital output signal to devices.
IN ARM7
  2 legacy ports (Port 0, Port 1)
  Each port has 32 pins (P0.4 means Port 0 pin 4)

## Slide 4: LPC 2388 Board

## Slide 5: LPC 2388 Board (Available Port)
Port 0
  P0.0, P0.1 (2 pins continuous)
  P0.4 – P0.9 (6 pins continuous)
  P0.12 – P0.18 (7 pins continuous)
  P0.24 – P0.31 (8 pins continuous)
Port 1
  P1.19 – P1.31 (13 pins continuous)

## Slide 6: Control Register on GPIO Port
There are 4 abstract registers to control GPIO port
  IODIR (GPIO Port Direction Control Register)
    To control either GPIO port is an input port (0) or output port(1)
    We use IODIR0 for Port0, and IODIR1 for Port1
  IOPIN (GPIO Pin Value Register)
    To read current port status
    We use IOPIN0 for Port0, and IOPIN1 for Port1
  IOSET (GPIO Port Output Set Register)
    To write data “1” to the specific port to make output logic to “1”
    IOSET0 for Port0, and IOSET1 for Port1
  IOCLR (GPIO Port Output Clear Register)
    To write data “1” to the specific port to make output logic to “0”
    IOCLR0 for Port0, and IOCLR1 for Port1

## Slide 7: Example 1 : Setting a port as output
unsigned int P0_9 = 0x00000100;
IODIR0 = P0_9;
IOSET0 = P0_9;
IOCLR0 = P0_9;
Define a variable P0_9 to store value 0x00000100
Set Port 0.9 as an output port
Set logic “1” as output of Port 0.9
Set logic “0” as output of Port 0.9

## Slide 8: Example: 2 LEDs Blink (1)
2 LEDs
  connected to P0.29
  connected to P0.30
We want 2 LEDs blink at the same time.

## Slide 9: Example: 2 LEDs Blink (2)
#include “LPC23XX.h”
int main(void) {
unsigned int P0_29 = (1 << 29);
unsigned int P0_30 = (1 << 30);
int i;
IODIR0 = P0_29 | P0_30;
while(1) {
IOSET0 = P0_29 | P0_30;
for(i = 0; i < 10000; i++);
IOCLR0 = P0_29 | P0_30;
for(i = 0; i < 10000; i++)
}
}

## Slide 10: Example 3: 7-Segment (1)
Suppose, we use common cathode 7-segment
  Logic 1 at either a, b, c, d, e, f, g or dp will light up that LED.
We will use
  P1.31 for a
  P1.30 for b
  P1.29 for c
  P1.28 for d
  P1.27 for e
  P1.26 for f
  P1.25 for g
  P1.24 for dp

## Slide 11: Example 3: 7-Segment(2)
Display | P1.31 (a) | P1.30 (b) | P1.29 (c) | P1.28 (d) | P1.27 (e) | P1.26 (f) | P1.25 (g) | P1.24 (.) | Hex Value
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0xFC000000
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0x60000000
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  | 
. |  |  |  |  |  |  |  |  | 
Let’s complete the table

## Slide 12: Example 3 : 7-Segment (3)
Code for displaying “0” on 7-segment.
#include “LPC23XX.h”
int main(void) {
unsigned int P1_24TO31 = 0xFF000000;
IODIR1 = P1_24TO31;
IOCLR1 = P1_24TO31;
IOSET1 = 0xFC000000;
while(1);
}

## Slide 13: SWITCH-CASE
SWITCH-CASE in C is used for selecting a multiple (constant) choices.

## Slide 14: Example : SWITCH-CASE

## Slide 15: Example : SWITCH-CASE with Break

## Slide 16: Example : 7-Segment with SWITCH
#include “LPC23XX.h”
int main(void) {
unsigned int P1_24TO31 = 0xFF000000;
int num = 0;
IODIR1 = P1_24TO31;
IOCLR1 = P1_24TO31;
switch(num) {
case 0 : IOSET1= 0xFC000000; break;
case 1 : IOSET1 = 0x60000000; break;
…
}
while(1);
}

## Slide 17: Assignment 9
Write a program in C for microcontroller to display a number on
7-segment as a
following sequence
  “0”  “1”  “2”  “0”  “1”  “2”  “0”  …
  Don’t forget to wait for a moment before moving to the next number
  Don’t forget to clear last output before setting the new one
  Use “switch-case” and some loop statements for this program