## Slide 1: Input Interface
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Review : Control Register on GPIO Port
There are 4 abstract registers to control GPIO port
  IODIR (GPIO Port Direction Control Register)
    To control either GPIO port is an input port (0) or output port(1)
    We use IODIR0 for Port0, and IODIR1 for Port1
  IOPIN (GPIO Pin Value Register)
    To read current port status
    We use IOPIN0 for Port0, and IOPIN1 for Port1
  IOSET (GPIO Port Output Set Register)
    To write data “1” to the specific port to make output logic to “1”
    IOSET0 for Port0, and IOSET1 for Port1
  IOCLR (GPIO Port Output Clear Register)
    To write data “1” to the specific port to make output logic to “0”
    IOCLR0 for Port0, and IOCLR1 for Port1

## Slide 3: Setting a port as an INPUT port
Suppose that you want to set a port P0.0 as an Input port.
  IODIR0 = 0x0; //ALL Port 0.0 will be input port.
Normally an INPUT port without anything connect to it will return a logic “1” (high)
So If you want to take an input “1” to microcontroller, you need to supply a logic “0” (low)
We can check an INPUT port status by using IOPIN register

## Slide 4: How to connect a push button to microcontroller
While you do not push a switch, P0.0 has a logic “1”
When you push a switch, P0.0 has a logic “0”

## Slide 5: How to check whether switch is push or not in a program
31 | 30 | . | . | . | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | . | . | . | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | . | . | . | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | . | . | . | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
#include “LPC23xx.h”
int main(void) {
unsigned int P0_0 = 0x1;
IODIR0 = 0x0;
while(1) {
if((IOPIN0 & P0_0) == 0)
{
//switch is pushed
} else {
//switch isn’t pushed
}
}
}
Bit
IOPIN0
Switch is not pushed
P0_0
IOPIN0 & P0_0
31 | 30 | . | . | . | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
1 | 1 | . | . | . | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | . | . | . | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | . | . | . | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bit
IOPIN0
Switch is pushed
P0_0
IOPIN0 & P0_0

## Slide 6: Example : 1 Push Button + 1 LED
We want to use
  P0.0 as an input connecting to a push button switch
  P0.1 as an output connecting to a LED
  When a push button is pressed, LED will be on.
  When a push button is not pressed, LED will be off.

## Slide 7: Example 1: Flow Chart

## Slide 8: Example 1 : Write a Program
#include “LPC23XX.h”
int main(void) {
unsigned int P0_0 = 0x1;
unsigned int P0_1 = 0x2;
IODIR0 = P0_1;
IOCLR0 = P0_1;
while(1) {
if((IOPIN0 & P0_0) == 0)
IOSET0 = P0_1;
else
IOCLR0 = P0_1;
}
}

## Slide 9: Example 2 : 2 Switches + 2 LEDs
We want to use
  P0.0, P0.1 as input ports connecting to push button switches
  P0.4, P0.5 as an output connecting to a LED
  When a push button P0.0 is pressed, LED connecting to P0.4 will be on.
  When a push button P0.1 is pressed, LED connecting to P0.5 will be on.

## Slide 10: Example 2: Flow Chart
P0.0
P0.4
P0.1
P0.5

## Slide 11: Example 2: Write a Program (1)
#include “LPC23XX.h”
int main(void) {
unsigned int P0_0 = (1 << 0);
unsigned int P0_1 = (1 << 1);
unsigned int P0_4 = (1 << 4);
unsigned int P0_5 = (1 << 5);
IODIR0 = P0_4 | P0_5;
IOCLR0 = P0_4 | P0_5;
//Code on the next slide
}

## Slide 12: Example 2: Write a Program (2)
while (1) {
if((IOPIN0 & P0_0) == 0) {
IOSET0 = P0_4;
} else {
IOCLR0 = P0_4;
}
if((IOPIN0 & P0_1) == 0) {
IOSET0 = P0_5;
} else {
IOCLR0 = P0_5;
}
}

## Slide 13: Example 3: Code Complete
#include “LPC23XX.h”
int main(void) {
unsigned int P0_0 = (1 << 0);
unsigned int P0_1 = (1 << 1);
unsigned int P0_4 = (1 << 4);
unsigned int P0_5 = (1 << 5);
IODIR0 = P0_4 | P0_5;
IOCLR0 = P0_4 | P0_5;
while (1) {
if((IOPIN0 & P0_0) == 0) {
IOSET0 = P0_4;
} else {
IOCLR0 = P0_4;
}
if((IOPIN0 & P0_1) == 0) {
IOSET0 = P0_5;
} else {
IOCLR0 = P0_5;
}
}
}

## Slide 14: Life is not Easy 
When you use switch as input to your microcontroller to do more complex task than just turn on and off LED, it can have a “Contact bounce and De-bouncing” problem.
Contact bounce and De-bouncing
  Push-button switches, toggle switches, and electro-mechanical relays all have one thing in common: contacts.
  It's the metal contacts that make and break the circuit and carry the current in switches and relays.
  Because they are metal, contacts have mass. And since at least one of the contacts is on a movable strip of metal, it has springiness.

## Slide 15: Contact Bounce and De-Bouncing
If you use switch as input to your counter program.
  Let’s say, if you push a switch one time, counter will be increase the value by 1.
Suppose counter value is now 0
  From the figure above, what is the counter value after you press and release the switch ?

## Slide 16: Fixed Contact Bounce by Code (1)
Suppose, P0.0 is used as input port connecting to a push button switch

## Slide 17: Fixed Contact Bounce by Code (2)
if ((IOPIN0 & P0_0) == 0) {
Counter++;
}
if ((IOPIN0 & P0_0) == 0) {
for(i = 0; i < 2000; i++);
if ((IOPIN0 & P0_0) == 0) {
Counter++;
}
}

## Slide 18: Example3 : 7-Segment + 1 switch
We will use
  P0.0 as a input port connecting to a push button
  P1.24 – P1.31 for output to drive 7-segment
  7-segment displays “0” at the initial state
  After a user presses the switch, the 7-segment will display next number of its state
  If the number of 7-segments display is “9”, next time user presses the button the 7-segment will display “0”

## Slide 19: Example 3: 7-Segment
Display | P1.31 (a) | P1.30 (b) | P1.29 (c) | P1.28 (d) | P1.27 (e) | P1.26 (f) | P1.25 (g) | P1.24 (.) | Hex Value
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0xFC000000
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0x60000000
2 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0xDA000000
3 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0xF2000000
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0x66000000
5 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0xB6000000
6 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0xBE000000
7 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0xE0000000
8 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0xFE000000
9 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0xF6000000
. | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0x01000000

## Slide 20: Example 3 : Write a Program
#include “LPC23XX.h”
int main(void) {
unsigned int P1_24TO31 = 0xFF000000;
unsigned int P0_0 = 0x1; int Counter = 0, d;
IODIR1 = P1_24TO31;
IOCLR1 = P1_24TO31;
while(1) {
if((IOPIN0 & P0_0) == 0) {
for(d = 0; d <= 1000; d++);
if((IOPIN0 & P0_0) == 0) {
Counter++;
if(Counter > 9) Counter = 0;
}
IOCLR1 = P1_24TO31;
}
switch(Counter) {
case 0 : IOSET1 = 0xFC000000; break;
case 1 : IOSET1 = 0x60000000; break;
case 2 : IOSET1 = 0xDA000000; break;
case 3 : IOSET1 = 0xF2000000; break;
case 4 : IOSET1 = 0x66000000; break;
case 5 : IOSET1 = 0xB6000000; break;
case 6 : IOSET1 = 0xBE000000; break;
case 7 : IOSET1 = 0xE0000000; break;
case 8 : IOSET1 = 0xFE000000; break;
case 9 : IOSET1 = 0xF6000000; break;
} //end switch
} //end while
} //end main