## Slide 1: Memory hierarchy
353156 – Microprocessor
Asst. Prof. Dr. Choopan Rattanapoka and Asst. Prof. Dr. Suphot Chunwiphat

## Slide 2: Two 7-Segments Display
Last week, we control a 7-segment
How about two 7-segments if you want to display a number “53” on two 7-segment
Suppose we define a local variable
  unsigned int number = 53;
We can get the most significant digit (MSD) by
  unsigned int MSD = number / 10;
We can get the least significant digit (LSD) by
  unsigned int LSD = number % 10; OR
  unsigned int LSD = (number – (MSD * 10))

## Slide 3: Exercise 1
Suppose X = 1456;
  6 as the first digit
  5 as the second digit
  4 as the third digit
  1 as the fourth digit
How to write a program to store the first digit, the second digit, the third digit and the fourth digit of X in variable A, B, C, and D respectively ?

## Slide 4: Memory Hierarchy
We have learnt that CPU need to load instructions from RAM to register (Fetch)
Then, CPU decodes the instruction (Decode)
Then Execute the instruction (Execute)
RAM
CPU
ALU
Registers
Load/Store
However, transfer data between CPU and RAM is slow comparing to CPU processing speed

## Slide 5: Cache Level 1
The solution to fix the slow data transfer rate between CPU and RAM, The CPU manufacturer put a high speed memory called “cache” inside in CPU chip.
Thus, the set of instructions will be loaded from RAM to cache and then CPU can load instructions from cache
Cache L1 run at CPU clock speed, but it’s quite small
  Intel core-i7 has
    32 kB of instruction cache
    32 kB of data cache
RAM
CPU
ALU
Registers
Load/Store
Cache L1

## Slide 6: Cache Level 2
Only cache L1 is not enough to improve PC performance that much.
In the past, mainboard manufacturers put a faster memory as a buffer between CPU and RAM.
We call it “cache level 2” (cache L2)
As time goes by, The CPU manufacturers can make circuits inside CPU smaller and smaller. Thus, there is more space left on the CPU die.
CPU manufacturers put cache level2 inside CPU. (Normally cache L2 size is around 1 MB to 6 MB)
RAM
CPU
ALU
Registers
Cache L1
Cache L2
RAM
CPU
ALU
Registers
Cache L1
Cache L2

## Slide 7: CPU Core
Since CPU technology develops very fast. The circuits inside CPU becomes smaller and smaller.
The CPU manufacturers decides to fill up the die with multiple ALU, cache, and registers (core)
In theory, CPU can do more than 1 instruction at a time
CPU
ALU
Registers
Cache L1
Cache L2
ALU
Registers
Cache L1
Cache L2
Core
Core

## Slide 8: CPU : 1 core VS 2 cores
CPU
ALU
Registers
Cache L1
Cache L2
CPU
ALU
Registers
Cache L1
Cache L2
ALU
Registers
Cache L1
Cache L2
Core
Core

## Slide 9: Cache Level 3
CPU core2 family (core2-duo, core2-quad) has only cache L2
However in core-i family (core-i3, core-i5, core-i7), Intel put cache L3 in CPU. This cache is shared for all the cores in chip
Cache L3 size is around 8MB

## Slide 10: Virtual Memory
Remind you that programs need to be loaded to RAM.
CPU can’t read instruction or data from harddisk directly.
How about some software such as game ?
  For example: Game size is 8 GB
  But your PC has RAM only 4 GB (can you play this game?)
We need to extend RAM size to fit software size
  Operating System (OS) use some part of harddisk to act as a RAM extension, we call it “Virtual Memory”
  Normally Virtual Memory size is about 2 – 2.5 times of RAM size

## Slide 11: Memory Conclusion (1)
Harddisk
Virtual Memory
RAM

## Slide 12: Memory Conclusion (2)
Levels in memory hierarchy
Central Processor Unit (CPU)
Size of memory at each level
Cache L1
Cache L2
Virtual Memory
Increasing Distance from CPU, Decreasing cost / MB
“Upper”
“Lower”
Cache L3
RAM